MSYS

                    A Multi-User, Multi-Port, Multi-Function 

                                Packet Radio BBS


                             By Mike Pechura, WA8BXN

                    (C) Copyright 1989 By HUB COMPUTERS, INC.
                              All rights reserved.

                             Version 1.02 March 1989

                      MSYS Documentation Table of Contents

        MSYS Installation Instructions                          1
        SETUP.EXE                                               2
        MSYS Command Summary                                    8
        MSYS SYSOP Commands                                     12                     
        MSYS BBS Commands                                       27
        DATADASE HELP                                           33
        Forward File Description                                35
        MSYS General information file                           43
        CHKMAIL/LFA/MRESTORE/MAILSIZE/BBSLIST                   47
        EDITVIEW (ED Command)                                   49
        EDITFILE (EF Command)                                   50
        HOUSECLEANING (HC command)                              52 
        Sysop commands related to TCP/IP                        54
        Samples of MSYS files                                   57
        BIT PATTERN CHART                                       60
        Frequent problems                                       61
        INFORMATION FOR USERS OF VERSION 1.01                   62
        Index                                                   64


        Thanks to N8HTG/NT8V for help with this documentation!




















                                   1




                        MSYS Installation Instructions #
                    (c) Copyright 1989 by HUB COMPUTERS, INC.

             Installation  of MSYS is not particularly difficult but  you 
        should follow the following steps in order.

        1.  Make a backup copy of the distribution disk. You  can  either 
        copy  the  entire disk with Diskcopy or do the  individual  files 
        with  copy. Be sure to copy all the directories if you  copy  the 
        individual files. Then print the files in the DOC directory. Read 
        through all of them before proceeding.

        2. Make a default directory on your hard disk. I call mine  MSYS. 
        Use the command:  md c:\msys

        3. Go to the default directory: cd c:\msys

        4.  Copy the root directory files from the distribution  disk  to 
        the default directory: copy a:\*.* c:\msys

        5. Make required subdirectories: md c:\msys\mail
                                         md c:\msys\files
                                         md c:\msys\help

        6.  Copy  the  help files from distribution  disk:  
                                         copy  a:\help c:\msys\help

        8.  Edit  the file c:\msys\msys.opt with  your  favorite  program 
        editor. See documentation on setup for details.

        9. Run SETUP.EXE to create c:\msys\msys.def

        10. Make sure you have at least 
        files=20
        in your config.sys file in the root directory of your boot disk.

        11. Using any ASCII editor, create MSYSFWD.DEF. If you don't know 
        what to put it in now, put the following (to be replaced later):
        F0 WA8BXN
        WA8BXN
        --------
        12. Type MSYS and it should begin to run!

        13. Type MERge. You can ignore any messages about MSYSBBSB.DAT at 
        this time.

        *** Special Note
        Determining  the  type of monitor you have: If you have  a  color 
        monitor, the default is ok. If you have a monochrome monitor that 
        uses and RCA phono pin plug then you also are using a Color 
        Graphics Adapter interface card and the default should be ok. If 
        you can do the command MODE MONO (this is a DOS command) and not 
        get any error messages and the computer continues to work, you 
        probably have a monochrome (TTL) interface card. You will need
        to specify WINDOW DISPLAY MONOCHROME in your MSYS.OPT file.


                                   1




                                   SETUP.EXE #
                    (c) Copyright 1989 by HUB COMPUTERS, INC.

             Before MSYS can be used a configuration file (MSYS.OPT) must 
        be  created and the program SETUP.EXE must be run to  create  the 
        file MSYS.DEF. The file MSYS.OPT is a standard ASCII file and may 
        be created with any program editor. The basic format of the  file 
        is:

        PORT number AT number INT number SPEED number [NAME description]
        PORT number SUBPORT number OF [PORT] number [NAME description]
        DIGI callsign FROM [PORT] number TO [PORT] number [AS callsign]
        NUMCHANS number
        BBS       CALL      callsign
        BBS       ALIAS     callsign
        KANODE    CALL      callsign
        ANSWER    CALL      callsign
        FORWARD   CALL      callsign
        ID        CALL      callsign
        ID        EVERY     number
        AX25      FRACK     number
        AX25      MAXFRAMES number
        AX25      RETRIES   number
        AX25      CHECK     number
        MONITOR   IFRAMES   on/off
        MONITOR   UFRAMES   on/off
        MONITOR   SFRAMES   on/off
        MONITOR   BFRAMES   on/off
        MONITOR   OUTGOING  on/off
        MONITOR   PORTS     mask
        WINDOW    number    SIZE number number number number
        WINDOW    number    BACKGROUND number
        WINDOW    number    FOREGROUND number
        WINDOW    number    PAGE number
        WINDOW    UNUSED    BACKGROUND number
        WINDOW    UNUSED    FOREGROUND number
        WINDOW    DISPLAY   color/monochrome
        PROCESS   processname [WINDOW] number
        STACK     processname number
        SYSOP     NAME      name
        SYSOP     QTH       location
        SYSOP     ZIP       zip code
        MAKE

        Notes: 
             1. Items enclosed in square brackets ([...]) are optional
             2. Numbers assumed in decimal unless prefixed by $ then hex
                is assumed
             3. on/off means the word ON or OFF
             4. mask is the numeric representation of a bit string with 
                the rightmost bit corresponding to port 0. 1=to be 
                monitored
             5. Where more than 1 space is shown, 1 or more space are ok
             6. Callsign can include SSID (-number)
             7. Ordering of the statements is generally not important


                                   2




             8. If there is an * at the beginning of a line it is ignored
             Output from the execution of SETUP.EXE is the file  MSYS.DEF 
        (a  binary file) and a listing to the display console (which  may 
        be  routed  to the printer via redirection:  SETUP  >LPT1:).  The 
        listing  consists  of two parts: the  original  input  statements 
        followed  by a complete list of all options generated  (including 
        defaults). 
             If  any errors are detected, the MSYS.DEF file will  not  be 
        created. A sample of a MSYS.OPT file is found in MSYS.OPT on  the 
        distribution disk.

                       Explanation of each statement type
                       -----------------------------------
        PORT number AT number INT number SPEED number [NAME description]
        PORT number SUBPORT number OF [PORT] number [NAME description]
             The PORT statement has the above two variations. The  number 
        following the word PORT is the port number. It must be between  0 
        and  4.  The  version containing the word AT  defines  an  actual 
        serial  interface  while  the SUBPORT version  defines  a  second 
        logical port for multiport TNCs such as the KPC-4. There must  be 
        one PORT statement for each port to be used. Assign port  numbers 
        beginning with 0 in increments of 1.
             Following the word AT is the base I/O address of the 8250 in 
        the  serial  port, such as $3F8. Following the word  INT  is  the 
        interrupt number for the 8250, such as 4. After SPEED is the baud 
        rate to be used, such as 1200. Optionally the word NAME  followed 
        by some description of the port can be given. A good  description 
        would be the corresponding radio frequency.
             For  the  other  form  of the  PORT  statement,  the  number 
        following  the  word  SUBPORT  is  the  logical  channel  number, 
        typically  1  for  the  KPC-4. Next comes  the  word  OF  in  the 
        statement  optionally followed by the word PORT. Next  comes  the 
        port  number  of a port statement defining an  actual  port  (ie, 
        contains  the word AT in its definition). The optional  NAME  and 
        description is the same as above.

        PORT description lines can also have two additional parameters: 

        RADIOSPEED bitrate# TNCTYPE #

        RADIOSPEED specifies the bit rate used by the TNC to the radio
        (300 or 1200 probably). If 300 bps is selected, shortened
        prompts are used in the BBS and perhaps elsewhere.

        TNCTYPE is a number from 0 to 999. Tnc type 0 is a KPC-x.
        Any other number causes a file MSYSTNC.# to be read for
        initialization statements to be sent to the TNC.

        * These parameters would be used for a tnc other than a KPC-X *

        For example:

        PORT  2  AT  $2F8 INT3 SPEED 4800  NAME  145.01  RADIOSPEED  1200 
        TNCTYPE 1



                                   3




        AND IN THE MSYSTNC.1 FILE YOU WOULD HAVE THE COMMANDS THAT  WOULD 
        PUT YOUR TNC INTO KISS MODE.

        DIGI callsign FROM [PORT] number TO [PORT] number [AS callsign]
             The  DIGI  statement defines a digipeater  callsign.  Repeat 
        this statement type up to 25 times as desired. The first callsign 
        is  the callsign that would be used in the VIA list by a  station 
        trying  to  use the digipeater. The port  number  following  FROM 
        indicates  the  port that will be using this call.  The  TO  port 
        number indicated the port on which packets having this the  first 
        callsign  as  digipeater  should  be  output  on.  For  a  normal 
        digipeater  the two port numbers will be the same; for a  gateway 
        they  will  be different. The optional AS  callsign  specifies  a 
        replacement  for the first callsign in the digipeater  list  when 
        the packet is sent out the TO port. If omitted the first callsign 
        is assumed (ie, no change). Consider the following examples:
                  DIGI MYDIGI FROM 0 TO 0
                  DIGI MYDIGI FROM 1 TO 1
                  DIGI W1XX-3 FROM 0 to 0
        This  would allow the callsign MYDIGI to be used in the via  list 
        on  either port 0 or 1. The packet is retransmitted on  the  same 
        port it it heard on. The call W1XX-3 can also be used to digipeat 
        on port 0.

                  DIGI MYGATE FROM 0 TO 1
                  DIGI MYGATE FROM 1 TO 0

        This  pair would define a gateway between ports 0 and 1 with  the 
        callsign MYGATE used in both directions.
                  
                  DIGI TOF1 FROM 0 TO 1 AS TOF2
                  DIGI TOF2 FROM 1 TO 0 AS TOF1

             This  interesting pair allows TOF1 to be used as  a  gateway 
        digipeater call on port 0 (no effect if used on port 1). When the 
        packet is repeated it will have TOF2 in the digipeater list where 
        TOF1 originally was. The opposite is true on port 1: When TOF2 is 
        used  as a digipeater call the packet is repeated on port 0  with 
        TOF1 being substituted for TOF2. The substitution is  transparent 
        to the users.

        NUMCHANS number
             NUMCHANS  is used to specify the number of logical  channels 
        that  will be allocated. Each connection (while  connected)  uses 
        one  logical  channel. When the KA Node is being  used  a  second 
        logical  channel  is  used for outgoing  connects.  Each  logical 
        channel requires about 7K of memory. They are available for reuse 
        when a station disconnects.

        BBS       CALL      callsign
             This  statement gives the callsign that can be connected  to 
        for  the  "big"  BBS.  The callsign can  contain  an  SSID.  This 
        statement is also optional; if omitted stations will not be  able 
        to connect to the BBS unless a BBS ALIAS is given.
             


                                   4




        BBS       ALIAS     callsign
             This  statement gives the callsign that can be connected  to 
        for  the  "big"  BBS.  The callsign can  contain  an  SSID.  This 
        statement is also optional; if omitted stations will not be  able 
        to connect to the BBS unless a BBS CALL is given.
             
        KANODE    CALL      callsign
             This  statement gives the callsign of the KA Node  which  is 
        similar  to  the  KA Node provided in the  Kantronics  tncs.  The 
        callsign  can  (and  probably  should)  contain  an  SSID.   This 
        statement  is optional; if omitted stations will not be  able  to 
        connect to the PBBS.

        ANSWER    CALL      callsign
             This  statement gives the callsign that can be connected  to 
        by stations wanting to talk to the SYSOP. It is also used as  the 
        callsign when the Connect command is used. The callsign can  (and 
        maybe  should)  contain  an SSID. This statement  should  not  be 
        omitted.

        FORWARD   CALL      callsign
             This  statement  gives  the callsign used when  the  BBS  is 
        forwarding.  It can (and probably should) contain and SSID.  This 
        statement should not be omitted if the BBS is to be used.

        ID        CALL      callsign
             This  statement  gives the callsign that will  be  used  for 
        identification purposes. It must be your actual amateur  callsign 
        and  should  NOT have an SSID specified. This statement  MUST  be 
        used.

        ID        EVERY     number
             This statement specifies the number of minutes between  IDs. 
        The  list of stations for which there is mail is  generated  with 
        every ID.

        AX25      FRACK     number
             Number   is   the   number  of  seconds   to   wait   before 
        retransmitting  a  packet. All of the AX25  statement  forms  are 
        optional.

        AX25      MAXFRAMES number
             Number  specifies the maximum number of frames that  can  be 
        outstanding before waiting for an ACK. Must be between 1 and 7.

        AX25      RETRIES   number
             This  is  the  number of retries that will  be  made  before 
        abandoning a connection.

        AX25      CHECK     number
             If  there is no activity on a logical channel for  10  times 
        this number of seconds there will be an automatic disconnect.

        MONITOR   IFRAMES   on/off
             Turns  on or off the displaying of Information  frames.  All 


                                   5




        forms of the MONITOR statement are optional.
        MONITOR   UFRAMES   on/off
             Turns on or off the displaying of Un-numbered frames (except 
        beacons, see below).

        MONITOR   SFRAMES   on/off
             Turns on or off the displaying of System frames.

        MONITOR   BFRAMES   on/off
             Turns on or off the displaying of Beacon frames (Un-numbered 
        information).

        MONITOR   OUTGOING  on/off
             Turns on or off the displaying of all outgoing packets.

        MONITOR   PORTS     mask
             Determines which ports will be monitored. The rightmost  bit 
        of  this number corresponds to port 0, the next bit to  the  left 
        port  1 and so on. Ports with 1 bits are displayed  (as  selected 
        above). A value of 13 (decimal, $D in hex) would enable ports  0, 
        2 and 3, for example.

        WINDOW    number    SIZE number number number number
             This  form of the window statement gives the bounds  of  the 
        window  whose  number is given after the word  WINDOW.  The  four 
        numbers after the word SIZE are the upper left column (1 to  80), 
        the  upper  left row (1 to 25), the lower right column,  and  the 
        lower  right row respectively. All of the WINDOW statement  forms 
        are optional and should be used with great caution.

        WINDOW    number    BACKGROUND number
        WINDOW    number    FOREGROUND number
             These two forms of the WINDOW statement give the  background 
        and  foreground  colors of the window specified  after  the  word 
        WINDOW.  The rightmost number is a color number from 0 to 15  for 
        foregrounds and 0 to 7 for backgrounds. The corresponding  colors 
        are:
        Black    0     Blue    1    Green    2       Cyan    3  Red     4
        Magenta  5     Brown   6    Lt Gray  7       Gray    8  Lt Blue 9
        Lt Green 10    Lt Cyan 11   Lt Red   12      Lt Mag  13 Yellow 14
        White    15

        WINDOW    number    PAGE number
             This statement assigns a window to the specified page (0-3).

        WINDOW    UNUSED    BACKGROUND number
        WINDOW    UNUSED    FOREGROUND number
             These  two statements give background and foreground  colors 
        to the places on the screen not assigned to any window.

        WINDOW    DISPLAY   color/monochrome
             This statement selects the kind of display adapter you have, 
        COLOR or MONOCHROME. If you have a CGA card, select COLOR.




                                   6




        PROCESS   processname [WINDOW] number
             This  statement specifies the window that is to be used  for 
        output from the allowable process names. Be extremely careful  if 
        you use this statement.
        STACK     processname number
             This statement specifies the number of bytes to be allocated 
        for  the  stack  for the allowable process  names.  You  probably 
        shouldn't mess with the defaults!

        SYSOP     NAME      name
             You must use this statement to specify your first name.
        SYSOP     QTH       location
             You must use this statement to specify your location.

        SYSOP ZIP zip code
             You must use this statement to specify your zip code.

        MAKE
             Use  this statement if you want to produce the new  MSYS.DEF 
        file if there are no errors.

                  
        Here is a sample MSYS.OPT file for you to figure out!

        port 1 at $3e8 int 4 speed 1200 name  223.70
        port 0 at $2f8 int 3 speed 1200 name  145.01
        digi bxng from 0 to 0 as bxng
        digi bxng from 1 to 1 as bxng
        digi bxn501 from 0 to 0 as bxn501
        digi bxn501 from 1 to 0 as bxn370
        digi bxn370 from 0 to 1 as bxn501
        digi bxn370 from port 1 to port 1 as bxn370
        digi test-4 from port 0 to port 1 as test-5
        digi wa8bxn-3 from 0 to 0
        bbs call wa8bxn-13
        kanode call wa8bxn-1
        answer   call wa8bxn-14
        forward call wa8bxn-12
        sysop name Mike
        sysop qth Kirtland, OH
        sysop zip 00000
        id call wa8bxn
        window display color
        make













                                   7




                             MSYS Command Summary #
                    (c) Copyright 1989 by HUB COMPUTERS, INC.

             The following is a summary of the commands available at  the 
        local  keyboard for MSYS. The commands may be abbreviated to  the 
        capital letters.

        *comment  Enables comment line from user to SYSOP
        #msgs/use Displays total number of active msgs and known users on 
                  BBS
        ADDUser   Allows sysop to add a user to bbs
        APpend    Used to append a file to a message and  other  general 
                  uses
        ARchive   Puts given @BBS in specified subdirectory
        ARP       Lists the known callsign/IP address
        ARP ADD   Adds digipeaters to TCP/IP stations
        ARP DEL   Removes TCP/IP stations from arp list 
        AUtokill  Kill all messages after forwarding
        BAckuptim Specifies time to make backup
        BADuser   ON/OFF
        BBs       Enter the BBS as a local user
        BDigi     Specifies one digipeater for beacons
        BELLoff   Turns  bells on or off (on turns bell off   off  turns 
                  bell on)
        BMax      [port#] Max-BBS-connects
        BOOT      Remote sysop only
        BPorts    Used to indicate BBS ports only
        BText     Specifies one line of beacon text
        BUDCalls  Set  or  display the list of calls  with  SSID  to  be 
                  monitored
        BUDList   Turn on/off selective call monitoring
        C#        Attempt to connect to station via digi list  given  on 
                  port # 
        CHAnstat  Displays status of a logical channel whose number  is 
                  given       
        CHeck     Number  of  10  second intervals  of  no  activity  to 
                  disconnect
        CL B #    Change border color 
        CLrscrn   Clear  window  number given or  *  for  clear  all 
                  windows
        CMdwindow Specifies the window number to be used for commands (CM 
                  4)
        COpy      sourcepathname destpathname (include drive: if needed)
        CRetries  Sets number of retries for forward connect attempt
        DEBug     Used to display or modify memory
        DELEfile  Specifies file name to delete
        DELUser   Deletes a user from the user list
        DFree     Displays amount of disk space free
        DIGipeats Displays digipeater/gateway list
        DIRectory Displays  directory  for path  specified  Example  DIR 
                  mail\*.*
        DISconnec Forces a disconnect on logical channel specified
        DOcmdfile To execute a command file 
        DPorts    Allows sysop to selectively disable digipeater
        DTimedate Displays current date and time


                                   8




        EDit      Screen editor for files
        EFile     Edits the specified file
        EMsghdr   Edits the header of the specified msg number in BBS
        EUser     Edits specified user
        FBbstimes Allows specification of hours bbs is full function
        FCall     Finds the logical channel(s) in use by given callsign
        FIle      Converts specified msg number into file name given.
        FOrward   Initiates forwarding immediately
        FRAck     Displays or sets time in seconds to retransmit a packet
        FREe      Deallocates the logical channel specified
        FSize     Displays the file size for the pathname specified
        FTime     Forward time
        FTPgm     File Transfer Protocol
        F2#       Number  of seconds to  continue  displaying  monitored 
                  packets after F2 (function key) was last pressed.
        Getmsgotd Reads and displays message of the day file
        GRep      Will search the given file for the specified pattern
        HClean    This command automatically deletes specified messages.
        HDrs      Allows you to create file out of mesage
        Help      Lists the names of the commands
        HOstname  Hosts id name TCP/IP
        ID        Forces transmission of an ID immediately (also mail for 
                  list)
        IGnore    Calls in budcalls list will not be monitored
        JBbs      Lists (P)BBSs heard and their paths
        JDidipeat Lists Digipeaters heard and their paths
        JGateways Lists Gateways heard and their paths
        JHeard    Lists stations heard and those connected to BBS
        JKanodes  Lists KA Nodes heard and their paths
        JMsys     List other MSYS systems heard
        JNetrom   Lists NET/ROM nodes heard and their paths
        JTcp/ip   Lists TCP/IP stations and their addresses
        KEybd     Assign keyboard to channel number specified
        KIllproc  Abort specified process number (Can be hazardous!)
        KPorts    Allows sysop to selectively disable k Node
        LCount    Counts number of lines, characters,and words in file. 
                  (LC Filename)
        LOCKkbd   Locks the keyboard
        LUsers    List known user calls that have connected to BBS
        MAKEPriva On/off {sets/resets making messages private by default}
        MAXFrames Display or change number of frames sent before ACK rcvd
        MAXRead   Specifies maximum size message that can be read or file 
                  that can be downloaded 
        MCon      Number of connects allowed to sysop keyboard
        MDir      Creates given directory
        MEMory    Display amount of memory free
        MERge     Reads MSYSFWD.DEF and copies it to MSYS.FWD
        MHclear   Clears various J heard lists
        MONBframe Enable/disable monitoring of Beacon (UI) frames
        MONxx     Enable/disable  monitoring  of  PIDs  on   screen   2 
                  monitoring
        MONIFrame Enable/disable monitoring of Information frames
        MONITor   Enable/disable monitoring of incoming frames
        MONOutgoi Enable/disable display of outgoing frames
        MONPorts  Select which ports to monitor (bit string, LSB=port 0)


                                   9




        MONSframe Enable/disable monitoring of Supervisory frames
        MONSTats  Enables/disables recording of chan usage stats
        MONUframe Enable/disable monitoring of Un-numbered frames
        MYAlias   Display or change bbs alias callsign
        MYBbs     Display or change bbs primary callsign
        MYCall    Display or change Call/Answer callsign
        MYKnode   Display or change K Node callsign
        MYIpaddr  Sets IP address that the system will respond to.
        MYTcpcall Callsign used when sending arp and TCP/IP frames
        PAClen    Specifies  maximum number of bytes that are put  in  a 
                  packet
        PATh      Display information about given user callsign
        PForward  Display information about given BBS callsign
        POrts     Display information about ports
        PRInt     Prints a file (on printer) 
        PROcesses Display status of processes
        PRTmsgs   Enable/disable printing of messages     
        PWindow   Sets window to be used by a process
        QUIT      Terminates execution of MSYS gracefully more or less
        RDir      Removes the given directory
        REName    Oldpathname newpathname (must both be on same drive)
        REPlaces  Replaces incomming @BBS calls
        RESpons#  Number  of  seconds  to waite  before  sending  out  a 
                  response
        RETries   Displays or sets number of retries before disconnecting
        SEnd      Sends a line of text to specified channel: SE 1 The msg
        SMTP      Simple Mail Transfer Protocol
        SMes      List  sendme request queued or to remove  one  of  the 
                  request
        SM ADD    Adds entry to the sendme quiue
        SNow      Enables/disable changing screen only during retrace
        SOrt      Will sort up to 200 eighty byte records
        STatus    Displays some status information
        SUspendtr Number  of  free bytes in input  buffers  below  which 
                  monitoring is turned off.
        TAbs      ON/OFF Default is on
        TELnet    Used to establish keyboard to keyboard connection
        TImezone  Allows entry of your time zone
        TPorts    Enables/disables ports for TCP/IP
        TYpe      Alows you to type a file
        Trace25   Enables/disables trace of AX.25 state changes
        TraceIP   Enables/disables trace of TCP/IP state changes   
        Users     Writes out all users to file
        Video     Displays or changes video monitor in use
        WAtch     Toggles watching of specified channel number
        WBackgrnd Sets background color for specified window
        WColors   Gives list of colors and their numbers
        Wforegrnd Sets foreground color for specified window
        WPage     Sets page number to display specified window
        WSize     Specifies coordinates for specified window
        Window    Displays current window definitions
        WHo       Displays current users/messages
        W?        Displays window number in upper left of each window
        <Esc>     



                                   10




        Function key usage: 
        F1 thru F4 select page to display (0 to 3 respectively)
        F6  causes  the  following characters to the next  return  to  be 
        treated as a command even if keyboard currently connected to some 
        other process (such as local bbs, etc.).

        Ctrl/F2  suspends activity on the monitor screen (F2).
        Ctrl/F3  displays number of characters waiting in input &  output 
        buffers for each port.

        Ctrl/F4 terminates MSYS as if QUIT command was used

        Ctrl/F5 is the same as the PRocesses command

        Ctrl/F6 assigns keyboard to command processor
          
        Most commands give information on their usage is you type command 
        name followed by a question mark. Example WS ?







































                                   11




                             MSYS SYSOP Commands  #
                    (c) Copyright 1989 by HUB COMPUTERS, INC.


        *comment    Enables comment line from user to SYSOP

        #msg\use    Displays total number of active msgs and known  users 
        on  BBS. The number of messages that can be on the bbs is set  by 
        the mailsize program and the maximum number of users is 500.    

        ADDUser  Format ADDUser callsign
        This will allow the sysop to add a user callsign to the user file
        without that station having to connect to the bbs. This can be
        useful in conjunction with the automatic @BBS generation. After 
        the new user has been added you automatically will EUsers for the
        callsign at which time you can fill in the desired fields.

        APpend   Sourcefile  destfile
        This  command  causes  the  source file to  be  appended  to  the 
        destination file. This command may be used to append a file to  a 
        message file, among other more general uses.

        ARchive  @BBS filename
        This command will concatenate all current msgs with @BBS given to
        FILES/filename.  No  compression  is  done.  Example:  ar  RLIBBS 
        RLINOTES/JUNK  (This assumes you have a RLINOTES subdirectory  in 
        the FILES directory)

        ARP ADD allows you to manually add (or put it in MSYS.DO)
        a station (and up to two digipeaters) to the arp list.
        Syntax:   ARP ADD callsign  port# ip-address [digi1 [digi2]]
        Examples: ARP ADD WA8BXN 0 44 70 4 8 K8OZ
                  ARP ADD N8HSP 2 44.70.4.10 WB8CQR-5 WB8APD

        ARP DELete allows you to remove a single entry from the table.
        Syntax:   ARP DEL callsign
        Example:  ARP DEL N8HSP

        ARP      Used  without an argument lists  the  known  callsign/IP 
        address correspondence determined by TElnet connects. An optional 
        argument, CLEAR, may be used to erase all of the ARP entries.

        AUtokill     Kill all messages after forwarding.

        BAckuptim   Specifies the time to make backup of the mail file.

        BADuser      Takes an operand of ON or OFF. When ON,the calls  in 
        the  BUDCall  list will be totally ignored by  the  system.  Such 
        stations  will  not  be  able to connect to  the  system  in  any 
        way(AX.25 or TCPIP) and will not be digipeated. Do NOT use  SSIDs 
        in  this list so that the listed calls can be used to  match  any 
        incoming  SSID  the  station may use. Try  to  avoid  using  this 
        facility unless really necessary as it does add some overhead  in 
        the processing of every packet received. Hopefully stations  that 
        misbehave  will  realize  that they can be  turned  off  and  not 


                                   12




        persist in their activity.
        BBs  Enter the BBS as a local user this command gets you into the 
        BBS  as  if  you  had  connected to the BBS,  with  a  few  minor 
        differences. Of course while you are using the BBS other stations 
        can  still  connect as usual. When  in the BBS you  use  the  BBS 
        command set (B,C,D,H,I,J,K,L,M,N,P,R,S,U,V,W,X,?,*). 
        If you use the L command you will see all messages including  the 
        private  ones. Likewise you can Read and Kill private messages. 
        Message texts can be gotten from files by going through the steps 
        of sending a message: use the S command to give destination 
        station and @BBS, then the title, and then simply ^Z for the 
        text.  Then do a LL 1 command to see the number assigned to the 
        message.  Exit the BBS using the B command then use the COpy 
        command to copy a file to replace the empty file in the MAIL 
        directory.  For example if the message was assigned a number of 
        123, then you might use the command CO tempfile mail/msg123.dat. 
        See the COpy command below for more details of its use.

        BDigi    -Lets you specify ONE digipeater for  beacons  (id,mail, 
        btext) Can be different for each port.

        BElloff  on/off       on makes it quiet, off is default

        BMax     This command limits the maximum number of connects on a 
        port.   BBS  connects are exempted from the limit but  count  for 
        other  users.  Normal users get a BUSY response when over  limit. 
        BM 1 allows 1 user per port.  BM [port#] max BBS connects. 

        BOOT     Boots computer (Remote sysop only)

        BPorts    This command is used to indicate which ports
        are  BBS ONLY connects. A one in the corresponding  bit  position 
        makes a port BBS ONLY. For example,   BP 5  would only allow  bbs 
        connects on ports 0 and 2. The default is no BBS only ports.
        If you do use this command to make BBS only ports, you better be
        sure to mark all the bbs stations with user flag of 2!

        BText   - Lets you specify 1 line of up to 80 characters of  your 
        own beacon text.  Can be different for each port.

        BUDCalls   Set  or  display the list of calls  with  SSID  to  be 
        monitored  This command is used in conjunction with  the  BUDLIST 
        command  below.  As operands you give a list of  callsigns,  with 
        SSIDs,  that are to be monitored.  The calls should be  separated 
        by  blanks.  To list the current setting of  BUDCalls,  type  the 
        command with no operands. Examples:
        budc w1xx w2xx-1 w2xx
        budcalls K9XXX
        budc

        BUDList   Turn on/off selective call monitoring
        To enable only those packets with calls in the BUDCalls list 
        to  be monitored use the command BUDL on. To monitor packets  for 
        all calls, use the command BUDL off. This is the default setting.



                                   13




        C#  Attempt to connect to station via digi list given on port # 
        This command is used to connect to another station.  The 
        letter C must be followed by a digit indicating the port number 
        to be used for the connection. This is followed by a space.  Next 
        comes an optional window number to be used for the conversation. 
        Next comes the callsign of the station you want to connect to, 
        with SSID if needed. Following this can come Via and a list of 
        digipeaters to use, separated by commas. Examples:
        c1 w1xxx
        c0 w2xxx v k2xxx
        c2 k3xxx-2 v n4xxx-3,a5xxx
        When   you  issue  this command the screen to  be  used  for  the 
        conversation will be cleared and you will see a line "Enter 
        converse for channel # port #". When connection is made you will 
        get a message "*** Connection established to callsign".  If the 
        attempt retries out (determined by the RETries value), you will 
        get the message "Quit converse for chan # because no connect!". 
        In this case the default CALL process window may show "*** 
        callsign busy" if this is why the connection could not be made.
        Pressing any key before getting one of these messages will 
        abort the connect attempt and return you to the current command 
        processor window.
        When you are connected to a station, you type lines to be 
        sent to the other station and will see lines typed by the other 
        station. Once you begin typing a line it will not be interrupted 
        by lines from the other station until you press return.  To 
        terminate the connection, type ^C, the letter d and press return.
        If you want to save what you are getting on disk, press the 
        \   key  three  times and then press return.  You  will  get  the 
        message "*** Capture file opened ***". All lines you receive will 
        be   displayed  as  usual as well as being written  to  the  file 
        CAPTURE.DAT.  Three \followed by return will alternately  suspend 
        and  resume the capturing of lines to disk.  When you  disconnect 
        (or get disconnected) the capture file will be closed. 
        Note  that the capture file name is always CAPTURE.DAT.  Anything 
        that  was  in the file before turning capture on  will  be  lost.  
        Thus you might want to rename the capture file (using the  REName 
        command).   This file can be viewed by using the TYpe command  or 
        edited  with the EFile command You could for example  connect  to 
        some  other  BBS,  read a message found there  after  turning  on 
        capture  and then use the capture file to replace a message  text 
        for one of your own messages.This procedure is explained in  more 
        detail for the BBs command above .

        CHAnlstat   Displays status of a logical channel whose number  is 
        given.  This  command  requires  an  active  channel  number   as   
        a  parameter.  Information  about the channel will be   displayed  
        in  response  to  this  command. The information   includes   the  
        Port  number  used, the call of the station connected to  and   a  
        status byte in hex.

        CHEck      Number  of  10  second intervals  of  no  activity  to 
        disconnect.  This   command specifies the number of  ten   second  
        intervals  after  which  if  there  has been no  activity  on   a  
        channel   a  disconnect will automatically be generated.  To  see 


                                   14




        what   value   is  currently  set,  give  the  command  with   no 
        parameters. 

        CLrscrn        Clear  window  number given or  *  for  clear  all 
        windows.  This  command clears the window number given. If  *  is  
        given  for  the  parameter,  all  windows  are  cleared.  If   no 
        parameters   are  given,  then the command  processor  window  is 
        cleared.

        CL B color# allows you to set the border color (used on all 
        screens). Use the WC command to see the color list. Default color 
        is black for the border. Any of the 16 colors (0-15) may be used.

        CMdwindow Specifies the window number to be used for commands
        This  command is used to change which window is used by  the 
        command  processor. The default command window is number 0  which 
        by  default is the upper half of display page 0. This command  is 
        useful when you want a larger window (to type a file for example) 
        to   be  used  by  some  command.  The  new  window  is   cleared 
        automatically by this command. You will then get the cmd: prompt.
        (page 0 =F1 page 1 = F2 etc.)

        COpy   Sourcepathname destpathname (include drive:  if needed)

        CRetries - Sets number of retries that there will be for forward
        connect attempt

        DEBug Used to display or modify memory
        Options for debug are: E segadr:disp allows you to modify  memory 
        at the given address.  D segadr:disp displays memory at the given 
        address.  All numbers are in hex. Q gets you out of  debug.   Any 
        non hex input to E gets you out of E.

        DELEfile    Specifies file name to delete
        This  command is used to delete a file. You must give  as  a 
        parameter  a  single  file  path  name  without  wildcards.   The 
        parameter  can  contain a drive  specification  and/or  directory 
        names for the given file.

        DELUser   Deletes a user from the user list
        This command removes a user call from the BBS user list. The 
        callsign  given as a parameter must match the a call seen on  the 
        list  produced  by  LUsers exactly  (including  case).  Use  this 
        command to remove users that haven't been active lately when  you 
        are getting near the capacity of the list (currently 500  users). 
        The  last  time  a  given station connected to  the  BBS  may  be 
        obtained by using the P command while in the BBS.

        DFree     Displays amount of disk space free
        This command displays the number of bytes free on a disk. If 
        no operands are given the space is for the default disk (normally 
        C). If a letter is given as a parameter, the number of free bytes 
        will  be given for that drive. Be sure the drive is ready  before 
        using this command. If its not and you get the DOS error message, 
        type I for ignore.


                                   15




        DIGipeats  Displays digipeater/gateway list
        This command displays the list of digipeater definitions.

        DIRectory  Displays  directory  for path  specified  Example  DIR 
        mail\*.* This  command displays a sorted directory listing.  Only  
        the names of the files (or directories) are given, not the sizes.  
        To  get  the  size of a file, use the  FSize  command   described  
        below. Names of directories are enclosed in <>. If no argument is 
        given,  you  will  get   a  directory  for  the  current  default 
        directory  (normally C:MSYS). To list some other directory,  give 
        the  path  to that directory and a file name of *.*.  Other  file  
        specifications can  be  given for a selective directory list.  If 
        you  include  a drive  specification in the pathname, be sure the 
        drive is  ready before using this command. Examples:
        dir mail\*.*
        dir a:*.*
        dir files\*.c

        DISconnec    Forces a disconnect on logical channel specified
        This command can be used to force a disconnect on the 
        specified active channel. It will rarely be needed.

        DOcmdfile       This command is used to execute a command file.

        DPorts mask  (see KPorts mask)   

        DTimedate     Displays current date and time
        This command displays what the computer thinks the current 
        data and time is. To change it you unfortunately must exit MSYS 
        and use the appropriate DOS commands. Time is(hh:mm:ss)

        EDit filename - screen editor for files. Escape gets to command
        mode, do help for command list

        EFile     Edits the specified file
        This  command is used to edit an ASCII file with records  <= 
        80 bytes in length. At least one operand is required which is the 
        pathname  to  the  file you want to edit. A  second  operand  may 
        optionally  be  given  that gives the size of the  work  area  in  
        lines 
        to be allocated (default is 200). See the separate  documentation 
        for EDITFILE for more information on the editor.

        EMsghdr      Edits the header of the specified msg number in BBS
        This command allows you to edit the fields of a message 
        header.  One operand is required which is the message number to 
        edit. This command also automatically sets the message length to 
        the  actual size of the associated message file. This is useful 
        when you have replaced a message file with some other file as 
        described above. This command is also useful to change the status 
        of messages to ALL (or others) that have not been marked as being 
        read  (but actually have been) so that they don't appear  in  the 
        MAIL FOR list sent out with each ID. If you press Esc when
        editing you will skip the current and remaining fields and see
        the  header  again.  This allows you to bypass  having  to  press 


                                   16




        return for all the fields you don't want to change.
        If you place a string of characters that begins with a period 
        after the message number, it will be appended to the existing 
        @BBS field of the given message. Thus if the @BBS of msg 123 was 
        WA8BXN then EM 123 .NTSOH would cause the @BBS field of msg 123 
        to become WA8BXN.NTSOH.

        EUser      Edits specified user
        Display the meanings of the possible flags bits. 

        FBbstimes - Allows specification of hours bbs is full function

        FCall     Finds the logical channel(s) in use by given callsign
        This command finds the channel associated with a callsign. 
        The single required operand is a callsign without SSID. All 
        channels in use by that callsign (with  any  SSID) will be 
        displayed giving the Port, process number and name and complete 
        callsign (with  SSID). This can be useful when you were in the 
        middle of a conversation with some station (and still connected) 
        but switched the keyboard to some other process (maybe the 
        command processor) and now want to get back to that conversation. 
        Use the KEyboard command with the appropriate process number to 
        do so.

        FIle     -  converts specified msg number into file  name  given. 
        (msg# filename.)
        This command removes the forwarding lines at the beginning of the 
        file  it  creates.  If  you really want  to  keep  them,  use  an 
        appropriate rename command instead.

        FOrward   Initiates forwarding immediately
        This command causes forwarding to begin immediately if it is 
        not currently going on. You might want to use this command  when 
        you have just entered a new message with an @BBS specification 
        that you want sent out now.
        FO[callsign] of a single station to immediately forward to.  This
        must  match the callsign (including SSID) found on the F line  in 
        the forward file.

        FRAck     Displays or sets time in seconds to retransmit a packet
        This  commands allows you to set or display the number of 
        seconds to wait for an acknowledgment to arrive for a packet that 
        is sent out. If it doesn't arrive within the number of seconds 
        specified the packet will be retransmitted. The retry count for 
        the channel will also be incremented. Making this parameter to 
        small will congest the channel and cause unwarranted disconnects. 
        The default is 6 seconds. If in doubt, err on the high side!
        (port number optional) 

        FREe      De-allocates the logical channel specified
        This command allows you to immediately release an  allocated 
        channel.  The  process  using  the channel will  see  this  as  a 
        disconnect.   This  command  will  not  be  needed  very   often. 
        Disconnecting  which frees the channel will  automatically  occur 
        after the CHEck interval has expired with no activity.


                                   17




        FSize     Displays the file size for the pathname specified
        This  command  can be used to determine the size of  a  disk 
        file.  One operand is required which is the pathname to the  file 
        you  want the size of. It may include a drive  specification  and 
        directory paths in addition to the file name. Wild cards are  not 
        allowed.  Be sure the drive containing the file is  ready  before 
        using this command.

        FTIME     Forward time
        This command sets the time in minutes after the hour that 
        forwarding will start.

        F2  #      #  is the number of  seconds  to  continue  displaying 
        monitored packets after F2 (function key) was last pressed.   The 
        default  is 600 seconds (10 minutes).  Thus 10 minutes after  you 
        last  press F2 monitoring will be turned off until you  press  F2 
        again.

        Getmsgotd Reads and displays message of the day file
        This  command causes the message of the day file  (MSYS.OTD) 
        to  be read and displayed. The message of the day is sent to  all 
        stations connecting to the BBS. You can create and/or change this 
        file using the EFile command. Keep the contents short! 

        GRep  (filename pattern)  will search the given file for the 
        specified pattern, displaying lines that match.
        Case is ignored in the search.

        FTP      Takes a host-id as an argument (it can be either  an  IP 
        address  in  the square brackets or a symbolic  IP  address).  It 
        establishes  a  connection  to the FTP server  of  the  specified 
        system. FTP is the File Transfer Protocol used in TCP/IP.

        HClean   This command alows you to automatically delete specified 
        messages  every day at specified time. (see  MSYS.HCL)   Operands 
        are:
                 
                 HC  -  <no operand> showes time in minutes  after  00:00                   
        (midnight) that housecleaning happens.
                 HC? - Gives a short description
                 HC#  -Sets the time for housecleaning in  minutes  after          
        00:00 (midnight)
                 HC NOW - Manually initiates housecleaning
                
        HDrs --- allows you to create file out of msg headers
        Usage: HDrs filename   (including drive/path if needed)
        You  will get a complete list, with BIDS and bits if present,  of 
        all  messages on the system. You can then print this file  or  do 
        anything else you want with it. I put it on diskette and take  it 
        to  another computer to be printed here. I can then mark  up  the 
        list  to use to delete all the old and/or duplicated files.  This 
        is easier than repeatedly doing L commands in the BBS and  taking 
        notes!

        HOstname    TCP/IP HOSTNAME


                                   18




        Help      Lists the names of the commands
        This command lists the names of the available commands  with 
        the required part of the command name in capital letters.


        ID        Forces transmission of an ID immediately
        This command will send out an ID on all the ports. You might 
        use it to see if all your radios go into transmit as they should. 
        It also will send out the MAIL FOR list so you could also use  it 
        to  see  who  there is mail for (this part is  displayed  on  the 
        screen, you will also see it when the ID is automatically  sent). 
        The  text of the ID is not displayed at this time, but  is  shown 
        once during initialization.

        IGNORE    on/off  Off is default
        When on calls in the budcalls list will not be monitored

        JBbs      Lists PBBS'S heard and their paths

        JDigipeat Lists Digipeaters heard and their paths
             JD command screens out funny callsigns.
             JD command also lists callsigns with /R in id.

        JGateways Lists Gateways heard and their paths

        JHeard    Lists stations heard and those connected to BBS or PBBS
             This command gives a list of the last 10 stations that  were 
        heard on the ports or connected to the BBS or PBBS.

        JKanodes  Lists KA Nodes heard and their paths

        JMsys     Lists other MSYS systems heard.

        JNetrom   Lists NET/ROM nodes heard and their paths 
             These  commands give the PBBS systems, KA Nodes  and  others 
        that  have been heard on the ports. A BBS is a system that  sends 
        out  a beacon that contains /B after what looks something like  a 
        callsign. A KA Node is identified by /N in its beacon to ID.  For 
        both  of  these commands the date, time, callsign  and  path  are 
        given. This pair of commands is useful to identify the PBBS  that 
        goes with a given KA Node.
        The Net nodes are also included. The real call for such nodes
        are given in []. Real Netroms get the real call in {}.     

        JTcp/ip  List TCP/IP stations and their addresses

        KEyboard  Assign keyboard to channel number specified
        When  you press a key, it is placed in the input  buffer  of 
        the  process  to  which  the  keyboard  is  logically  connected. 
        Initially  this  is the command process. When  you  give  certain 
        commands (such as BB, PB, C) the keyboard will be assigned to the 
        new  process  created  for  the  command.  When  the  process  is 
        terminated,  the keyboard is automatically assigned back  to  the 
        command scheduler. 
        The  KEyboard  command allows you to manually  reassign  the 


                                   19




        keyboard.  As  a  parameter you give the channel number  of  the 
        process   you   want  to have the keyboard.  You   can   get  the 
        channel number from the lower right part of the F1 screen. To get 
        the  keyboard back  to  the  command processor so you can   issue  
        this   command  either  press ^F6 to assign to  keyboard  to  the 
        command   processor  or  press  F6 to temporarily  send  keyboard 
        input  to   the   command process up to and  including  the  next 
        return key.

        KIllproc      Abort specified process number (Can be hazardous!)
        Never  use this command to kill a permanent process.  Better 
        yet, just don't use this command!

        KPorts mask
                         see monitor ports
        DPorts mask
        These commands allow you to selectively disable the K Node
        on  any ports or use of the ID call as a digipeater  (DPorts)  on 
        any  ports.  The  mask  works just like the  port  mask  for  the 
        MONPorts  cmd. A 1 bit enables the corresponding port,  with  the 
        rightmost  bit  corresponding to port 0. These commands  will  be 
        most useful for HF operations if you don't want the K node to  be 
        accessible to or from the HF port, for example.

        LCount   This command counts the number of lines, characters  and 
        words in a given file.  (LC filename with path)

        LOCKkbd  This  command  "locks" the keyboard  so  that  any  keys 
        pressed  are  ignored. I put it in for two reasons. First,  I  am 
        getting  RF  into  my keyboard from HF radios  and  it  generates 
        random  characters. Second, my 3 year old son sometimes likes  to 
        press the keys. To "unlock" the keyboard, simply type lock  again 
        (no  CR  needed this time). When unlocking the  keyboard,  "lock" 
        must be all LOWER case.

        LUsers    List known user calls that have connected to BBS
        Use  this  command  to  see  who  has  connected  and   more 
        importantly how many users are in the user file since it can hold 
        only 500 users currently.
        LU   takes  an  optional  argument  to  list  users  flagged   as 
        BAD,EXPert,LIMited,  or BBSsystem (new classification).  Example: 
        LU EXP

        MAKEPriva On/off {sets/resets making messages private by default}

        MAXFrames Display or change number of frames sent before ACK rcvd

        MAXRead - specifies maximum size message that can be read or file 
        that can be downloaded.

        MCon  specifies number of connects allowed to the sysop  keyboard
        at one time if MCon 1, only allows an incomming call to the 
        keyboard to be answered if there are no other keyboard 
        connections.  MCon 0 pervents all incoming keyboard requests. 



                                   20




        MDir  Makes specified directory

        MEMory   Display amount of memory free


        MERge     (no parameters, except for ? for info).
        This  command  reads  MSYSFWD.DEF  and  copies  it  to  MSYS.FWD, 
        expanding  any  include  files ($filename). A new  file  is  also 
        produced,MSYS.BBS  that  is a sorted list of all  possible  BBS's 
        that can be forwarded to (including things like ARRL, 44*,  etc). 
        This  command was added for 2 reasons: previously, if there  were 
        any  include  files in the MSYS.FWD files they did not  get  read 
        when  a pf command was used and secondly, the new file is  needed 
        for hierarchical forwarding.
        The leftmost part of the hierarchical route only is used for
        forwarding  and  the  contents of the new file  were  needed  for 
        efficient processing. So, the bottom line is rename your existing 
        MSYS.FWD file to MSYSFWD.DEF and then use the MERge command.  Any 
        future  changes  you make to your forward file must  be  done  to 
        MSYSFWD.DEF  followed  by use of the MERge  command.  Its  called 
        MERge because it merges in the include files by the way.
        MHclear [letter [port or B]] clears the various J heard lists
                MH clears everything
                MH D clears all digi's heard
                MH D 1 clears digi's heard on port 1
                letters  are HBKDN or G (Heard, Bbs's, K  Nodes,  Digi's, 
        Netroms)

        MONBframe Enable/disable monitoring of Beacon (UI) frames

        MONxx    -  Replaces MONCC, MONCF etc - now can specify  any  hex 
        value
        for PIDs to ignore on screen 2 monitoring

        MONIFrame Enable/disable monitoring of Information frames

        MONITor   Enable/disable monitoring of incoming frames
        This is the master command for monitoring packets heard.  If 
        this is set to OFF then there will be no monitoring. If set to ON 
        then the types of packets selected will be monitored for calls as 
        selected by BUDCalls on the ports set by MONPorts.

        MONOutgoi Enable/disable display of outgoing frames

        MONPorts  Select which ports to monitor (bit string, LSB=port 0)
        This  command if given no argument displays which ports  are
        to  be monitored (all defined ones by default). If an  number  is 
        given  for  an argument, its bit pattern determines  which  ports 
        will be monitored. The rightmost bit corresponds to port 0. A one 
        bit enables a channel for monitoring.

        MONSframe Enable/disable monitoring of Supervisory frames

        MONSTats   enables/disables recording of channel stats.  Defaults 
        to OFF.


                                   21




        MONUframe Enable/disable monitoring of Un-numbered frames
        This group of commands determines which kind of frames  will 
        be monitored. If no operand is given, then the current setting of 
        the  variable will be displayed. If a single parameter  is  given 
        (either ON or OFF), then the variable will be given that value.

        MYAlias - display or change bbs alias callsign

        MYBbs     - display or change bbs primary callsign

        MYCall    Display or change Call/Answer callsign
        This command displays your keyboard callsign if there is  no 
        argument,  or  sets the keyboard callsign (used  to  connect  and 
        respond to connects) to the call given as an argument  (including 
        SSID).

        MYKnode     - display or change K Node callsign
        MYIpaddr    - sets ip address that system will respond to 
        Takes four integers in the range 0 to 255. It sets the
        IP address that the system will respond to. Example: MYI 44 70  4 
        6  If  MYIpaddress is not specified, or set to  all  zeroes,  the 
        TCP/IP support will be inactive.

        MYTcpip     - displays or change TCP/IP callsign (with SSID) 
        Takes a callsign (with SSID) that will be used when sending
        arp and TCP/IP frames. It can be the same as the ID call in most
        cases.

        PAClen   -  specifies maximum number of bytes that are put  in  a 
        packet before it is sent. Return also sends current packet.

        PATh      - displays information about given user callsign  (same 
        as P on BBS)

        PForward  - displays information about given bbs callsign 
        (same as PF on BBS)
          
        POrts       Various  information  is  given  by   this   command. 
        Interesting to look at but may not be very useful.  POrt can have 
        operand  on/off.  When  off a port will not  respond  to  the  id 
        callsign  (with  any  SSID) and will no  longer  digipeat  or  be 
        usable from the K Node.  BBS will not id unless you use it.   Id 
        will be very short if it has to id (no text for the UI frame).
        If  you  call a station with the port off this  will  still  work 
        because  incomming  packets  from that station  don't  include  a 
        connect packet.

        PRInt     Prints a file (on printer) 
        The argument is the pathname to the file to print. Make sure 
        the  drive  is  ready before using this command.  Make  sure  the 
        printer is ready (and exists) before using this command. Printing 
        is done to LPT1: via BIOS calls. This command will queue up to 25
        print  requests.  Print with no operands lists the files  in  the 
        queue.



                                   22




        PROcesses Display status of processes
        This  command displays for each active process  its  number, 
        program running for that process, an integer parameter passed  to 
        the process (usually a port or channel number), the least  amount 
        of memory left in the stack for the process (labeled SPmin),  and 
        the  window  used  for  output  by  the  process.  Of  particular 
        importance  is SPmin if the system does bizarre things.  If  this 
        number  is  less than say 100 the stack is too small.  If  its  a 
        negative number, you have problems for sure!

        PRTmsgs  on/off  Enables printing of incoming messages as they 
        are received.

        PWindow   Sets window to be used by a process
        If  given one parameter this command displays the  name  and 
        window used by the given process number. If two numbers are given 
        as parameters, the first is the process and the second number  is 
        the window number to assign to that process.

        QUIT      Terminates execution of MSYS gracefully more or less
        After you use QUIT command (or CTRL/F4) the screen is cleared.
        JK etc information is saved when you do a QUIT and reloaded 
        when bbs is started again.

        RDir  Remove specified directory

        REName    Oldpathname newpathname (must be on same drive)

        REPlaces   Reads bbs call/@bbs replace file

        RESponsetime #   Where # is the number of seconds to wait before
        sending out a response. This is the T2 timer value in the ax.25
        spec.  If  you  set RES to 0 it will work  the  old  way,  always 
        sending  out  a  response to each I frame  received  as  soon  as 
        possible.  With non-zero values for RES, the responses are  held, 
        the  latest one replacing any one being held, until no  I  frames 
        have  been  received for the time given. It then  sends  out  its 
        response.

        REtries   Displays or sets number of retries before disconnecting

        SEnd      Sends a line of text to specified channel
        Parameters are an active channel number and the text of  the 
        message to send. The text is prefixed with "MESSAGE FROM SYSOP AT 
        id-callsign".  Use  this to give helpful hints to users  you  see 
        that are in trouble with the commands they are trying to use.

        SMTP     Allows local access to the SMTP server 
        (mainly for test purposes).

        SMes     This command is used to list the sendme requests  queued 
        or to remove one of the requests.  SM without any parameters list 
        the current requests.  SM callsign msg# removes that request from 
        the queue.



                                   23




        SM ADD      Callsign msg# as a command. For example, if you type
        SM ADD WA8BXN 100 it will have the same effect as if WA8BXN had
        connected to your BBS and issued the command SENDME 100. Use this
        form  of  the  SM  command when some  BBS  operator  asks  for  a 
        particular  message to be sent to him and he isn't familiar  with 
        the Sendme capability of MSYS.

        SNow      Enables/disable changing screen only during retrace
        If you have a CGA adapter and there is a lot of snow  during 
        screen changes (particularly when changing display pages with F1-
        F4) and you don't like it, set SNow to ON. Otherwise leave it off 
        and the display will run faster.

        SOrt      (filename) will sort up to 200 eighty byte records. 
        Useful to sort your forward include files in the /fwd directory 
        so you can find things there more easily.

        STatus    Displays some status information
        I  put  this one in for my own debugging (like some  of  the 
        other  information  displays). The current time is  in  something 
        like seconds since midnight of 1900. If any channels are open you 
        will learn very little by what you see, but state 5 is the normal 
        connected state number. The next to last part of this display  is 
        somewhat important. FREE is what is currently free in the  buffer 
        used to get characters from the TNC (an interrupt driven  routine 
        is  used).  LEAST  is  the smallest  amount  of  space  that  was 
        available. If lease is small (say less than 100) you've got  some 
        real problems. I don't think I've ever seen it go below 3000.  If 
        it  is  small it means that characters are coming  from  the  TNC 
        faster than they are being processed. You might try a lower  baud 
        rate between the computer and TNC but this probably won't  really 
        help the situation much. Dispatches per second is how many  times 
        per  second  each process was given control of the CPU.  If  this 
        goes to zero I'd worry a lot!
        Note: will only display information for real ports.

        SUspendtrace  #      Where # is the number of free bytes  in  the 
        input buffers below which the monitoring is turned off. There  is 
        1  buffer  of 4096 bytes for each serial port (tnc).  The  amount 
        free  at any time is given by the STatus command. When  the  free 
        space gets less than the SU value, F2 monitoring is turned off to 
        allow things to get processed more quickly. Default value is 2000 
        bytes. Again, F2 displays take a lot of time and when the  system 
        gets  behind  it is a good idea to turn off the updating  of  the 
        display. When the free space in all the buffers goes above the SU 
        value  tracing  is turned back on (unless  otherwise  suspended). 
        This function can be effectively disabled by setting SU to 0  and 
        then it will work as before.

        TAbs ON/OFF (when on tabs are expanded on local display; when off 
        a tab shows up as ^I). Default is ON.

        TElnet    Takes  an  IP address and  optional  server  number  as 
        parameters.



                                   24




        Examples:  TE [44.70.4.10]
                   te hsp             (hsp would have to be defined in
                                        MSYSHOST.NET)

        TImezone - allows entry of your time zone

        TPorts     Takes a port mask value as an argument. This number is 
        used the same way as in in the other similar commands: each port
        corresponds to a port (port 0 is the rightmost bit) and when the
        bit is set to 1 for a given port that port is available for
        TCP/IP use (particularly ARP broadcasts).

        TYpe      Allows you to type a file

        Trace25       Enables/disables trace of AX.25 state changes
        Here  the parameters are on or off and if you set it on  you 
        will  get  more stuff that you can't understand faster  than  you 
        ever wanted to see it!

        TraceIP       Enables/disables trace of TCP/IP

        Users filename - writes out all users info to file

        Video     Displays or changes video monitor in use
        You can change the monitor you want to use while the  system 
        is  running (using COLOR or MONOCHROME as a parameter). I've  got 
        both  connected  to my systems here (at the same time) so  it  is 
        meaningful  to switch back and forth on rare occasions  (like  to 
        see if it works). You probably ought to specify the one you  want 
        to use in your MSYS.OPT file and not otherwise use this command.

        WAtch     Toggles watching of specified channel number
        This  command  allows  you to see all that  occurs  in  both 
        directions  for the channel you specify. Watching is  turned  off 
        when the channel is closed or you use the WAtch command a  second 
        time  for that same channel. The lines that go to the screen  are 
        not labeled in any way, they are just sent to the screen. If  you 
        WAtch  more than one channel at a time it will work but  you  may 
        wonder  which line came from which channel. Using watch may  have 
        some  side  effects like resetting the window being used  by  the 
        process  using the channel you have selected. That's a  "feature" 
        of this program and will not be corrected!
        WBackgrnd     Sets background color for specified window
        This  command requires two parameters: Window#  and  Color#. 
        The color number should be between 0 and 7.

        WColors   Gives list of color names and their numbers     

        Wforegrnd     Sets foreground color for specified window
        This  command requires two parameters: Window#  and  Color#. 
        The color number should be between 0 and 15.

        WPage     Sets page number to display specified window
        This command requires two parameters: Window# and Page#. The 
        page number must currently be between 0 and 3.          


                                   25




        WSize     Specifies coordinates for specified window
        This command requires 5 parameters. The first is the window# 
        being defined. The remaining parameters are two pairs of  numbers 
        giving the upper left and lower right corners of the window.  The 
        pair  is  column  number  (1,80)  then  row  number  (1  to  25). 
        Overlapping  windows  may  produce amusing  results.  To  specify 
        window 3 as being the entire screen the following command may  be 
        used: WS 3 1 1 80 25

        Window    Displays current window definitions
        Use  of this command is a good way to see what numbers  mean 
        in the various window definition commands.

        WHo Displays current users and messages (Remote SYSOP only)

        W?        Displays window number in upper left of each window
        Use  of  this command is the easiest way to find  out  which 
        window is which!

        Function key usage: 
        F1 through F4 select page to display (0 to 3 respectively)

        F6  causes  the  following characters to the next  return  to  be 
        treated as a command even if keyboard currently connected to some 
        other process (such as local bbs, etc.).
          
        Ctrl/F2  suspends  activity on the monitor  screen.  ^F2  restores 
        normal  operation.  This is probably as close as  being  able  to 
        scroll the F2 screen that I will be implementing.

        Ctrl/F3  displays number of characters waiting in input &  output 
        buffers for each port.

        Ctrl/F4 terminates MSYS as if QUIT command was used

        Ctrl/F5 is the same as the PRocesses command

        Ctrl/F6 assigns keyboard to command processor
          
        Most commands give information on their usage is you type command 
        name followed by a question mark. Example WS ?
















                                   26




                               MSYS BBS Commands #
                    (c) Copyright 1989 by HUB COMPUTERS, INC.


        B - Bye                   N - Enter name/qth
        C - Conference            P - Path to station    
        D - Download              R - Read message       
        G - Search file           S - Send Message       
        H - Help                  W - What files             
        I - Information           V - Version                
        J - Calls heard           X - Expert-Mode            
        K - Kill message          U - Current users         
        L - List Messages         ?x- Info about command     
        M - Message of the day    * - Comment line                            
                      

        The Bye command disconnects you from the BBS. Use it when you are
        done!

        The Conference command allows you to see what stations are
        currently connected in conference mode. You can also enter the
        conference  or  start  one  if none  is  currently  active.  When 
        stations  are connected in conference mode anything typed by  one 
        station  is seen by all stations. All of the software to do  this 
        is  contained  in this system. Any TNC can be  used  by  stations 
        connected  in conference mode with any computer or  terminal.  In 
        some  respects  the overhead is rather high in terms  of  channel 
        utilization since a packet typed by one station is sent to all of 
        the stations in conference mode individually and acknowledged  by 
        each  station individually. Another mode of conferencing will  be 
        made  available  in  the  future  to  stations  with  KISS   mode 
        compatible  TNCs  and  IBM PCs (and  possibly  also  C-64s).  The 
        easiest  way to see what conference mode does now is to enter  it 
        using  the  C command. Even if you are the only  station  in  the 
        conference  you will get an idea of what you would see  if  there 
        were others. To terminate conference mode, simply disconnect from 
        the  system.   Several commands are possible when  in  Conference 
        mode.  All begin with control/Z (^Z). Some have parameters.  Here 
        is the list:

        ^ZA            To  add a DX station heard to  the  spotting  list 
        (Add)
        ^ZB           To disconnect from the system (Bye)
        ^ZD           To display the DX spotting list (Display)
        ^ZP  chan  #    To ask a station on BBS to  join  the  conference 
                        (Page)
        ^ZR           To go back to BBS (Return)
        ^ZU           To list the current stations on the BBS or
                      Conference Mode (Users)

        The list users command gives output like this:     WA8BXN (B/4)
        which means that WA8BXN is using the BBS and is on channel number 
        4. The 4 would be used with the Page command that asks WA8BXN  to 
        join  the conference.The DX spotting list commands (^ZA and  ^ZD) 
        allow adding to or displaying the 10 line buffer that may be used 


                                   27




        to report DX stations heard. The date,time and call of station 
        using the ^ZA command is automatically added to the remaining 
        characters on the ^ZA command line. Thus you might type ^ZA 
        XY0ABC on 14.112 listening up 20 for example. The ^ZA command 
        both adds what you type at the bottom of the list and will also 
        broadcast it to all stations in conference. Note that most of 
        what you get in response to these commands is NOT seen by other
        stations.

        The Download command is used to read a file stored on the system.
        The  format of the command is D filename  where filename  is  the 
        name of the file to download. To see what files are available for 
        downloading, use W or WN command.
        To   get   a  file  from  a  subdirectory   type   d   (directory 
        name\filename)

        The  G (for GREP, a Unix utility) command allows you to search  a 
        downloadable file for a specified string of characters,  printing 
        all lines that contain the string of characters. Case is  ignored 
        in the comparison. No wild cards (like ? or *) are recognized. 
        When you use this command you will be asked for a file name and 
        then a search string. For file name enter the name that you would 
        use if you were downloading the entire file. If you do not give 
        a file name, DATABASE.0 will be assumed.
             When the command is used the user will be asked for the file
        name to search and then the search pattern. FILES\ will be 
        prefixed to the file name the user gives; thus downloadable files 
        may be pattern searched.  
            The G command is not available when the BBS is in limited 
        service mode.

        The H command will give you a short description of the
        commands.  For more information about a particular command, type 
        ?x where x is the letter of the command.

        The I command by itself gives hardware configuration of this
        system. For example:

        This system runs on an IBM PC type computer and is written in  C. 
        It  uses  TNCs running in KISS mode which allows  all  the  fancy 
        stuff it does. 

        Location is Port Huron, Michigan
        Tnc's    KPC-4 
                 PK-232
        Frequency       Radio      Power      Antenna
        145.03          MOCOM 70    60 W      Isopole at 80 ft
        145.09          TR-7400A    30 W      Isopole at 30 ft

        If you have any questions please live a message or call

        ID gives a list of the ports and digipeaters/gateways available. 

        The J command lists stations recently heard on the various ports
        and stations that recently connected. Use the P command for  path 


                                   28




        to station that have connected at some time.
        For the following commands the sponsor's callsign is given
        in {curly brackets}. This is normally NOT the call you would use.
        This callsign is given to help identify some of the "mystery"
        callsigns used for nodes and digipeaters such as "MYDIGI".

        JD command gives a list of the Digipeaters that have been heard
        along with the date and time they were heard and the the path 
        to them.

        JK gives a list of the KA nodes that have been heard along 
        with the date and time they were heard and the path to them.     

        JG  command  gives a list of the Gateways that  have  been  heard 
        along
        with the date and time they were heard and the path to them.

        JM List other MSYS systems that have been heard.     

        JN command gives a list of the NET/ROM nodes that have been heard
        along with the date and time they were heard, the real callsign
        of the node and the path to them (most are direct).You can
        specify a port number as an argument to limit the display to just
        that port. For example, JK 1 would display the KA Nodes heard on
        port1 only.

        The K command is used to kill (delete) old messages from the
        system.You can kill only those messages that are to or from your
        station.   The format of the command is K, a space, and then  the 
        number  of  the  message to delete.   May  use  multiple  message 
        numbers separated by a space. Example: k 123 6789 1123.

        KM - To delete all messages TO you.
        KF - Kill messages that have been forwarded (sysop only)
        KT - Msg# to kill NTS traffic you are going to deliver.
        K* - Kill messages marked with type * (sysop only)
        K@ - kills all messages with given @BBS.(sysop only)  
             Example:      K@ arrl

        The List command list selected message headers. The following
        format are available:

        L           - List messages since you last used the B command
        LM          - List messages to or from you  (List Mine)
        LN          - List all messages not yet read 
        LT          - List NTS Traffic messages
        LL #        - List the last # messages 

        Example: LL 10       - Lists last 10 messages

        LO          - List messages older than date yymmdd given
        LU          - Lists unread messages to you
        LY          - Lists msgs that have been read but not deleted
        LW          - Lists msgs with type W (for weather)  
        L< callsign - List messages from callsign


                                   29




        Example: L< WA8BXN
        L> callsign - List messages to callsign                

        Example: L> WA8BXN

        L@ callsign - List messages being sent to BBS callsign 

        Example: L@ WA8BXN

        L #         - List messages >= given number            

        Example: L 827

        L # #       - List messages from # to #                

        Example: L 50 75

        L"string"   - Lists messages with given string in title
        (case insensitive)

        L'string'   - Lists messages with given string in title
        (case insensitive)

        Examples:  L'Pfb'   L"ID's"   l"Modem users"

        L$          - List messages with type $

        Example: L$

        Note:  Messages  that  are Private are shown only  to  Sender  or 
        Addressee.

        The M command may be used to display the Message of the Day. 
        Normally  this  message  (if not empty)  is  displayed  when  you 
        connect  if  you have selected Expert mode (?X for more  info  on 
        Expert mode). If
        you  have selected Expert mode, using the M command is  the  only 
        way to see any Message of the Day. If there is no message of  the 
        day,  you will simply get the next command prompt.The message  of 
        the  day  will  advise you of new features  and  other  important 
        information.

        N command can be used to register your name or QTH. You should
        enter both of these. To enter your name type N yourname.

        Example: N Mike

        To enter your QTH, use the command NQ yourqth.

        Example: NQ Kirtland, OH

        To enter your ZIP or Postal Code, use NZ code.

        Example: NZ 44026



                                   30




        To  enter the primary BBS that you look for your mail on  use  NH 
        callsign.

        Example: NH KB8CI

        The P command can be used to find the path last used by a station
        to connect to this system. The format is P callsign.  Example:  P 
        W1AW The information given comes from the station's use of the  N 
        commands  and  information  recorded by the  system.  Try  the  P 
        command  with your own call to check the information  the  system 
        has about you.

        The  PF command can be used to find out if this system knows  how 
        to forward mail to a particular BBS (what you would enter as @bbs 
        in  the S command).The port number and call of the BBS  to  which 
        the  message would be sent is displayed along with the  VIA  list 
        used for the connect. If Net/Rom or KA Nodes are used to  connect 
        to the BBS to which the message would be forwarded to the fact is 
        noted  but  the details are not given.  If this system  does  not 
        contain the requested BBS in its forward file
        you  get  a  message that the callsign is  unknown.  Example:  PF 
        WA8BXN

        The R command is used to read messages that appear when you do  a 
        L  command.  After the letter R and a space you should enter  the 
        number  of  the  mesage  to  read  or  multiple  message  numbers 
        separated by spaces. Example:r 725 1012 892.    

             RH - Gives complete forwarding information.
             RM - Read unread messages addressed to you. 
             RS - Reads all mail for SYSOP. 
        Note  that when you read mail for SYSOP it gets changed  to  mail 
        for Sysop so that it won't continue to show up as a new msg. 

             The Send command format:   Sx  to call @bbs
        Where x is message type (P=private)
        To call is destination callsign (without - number)
        @bbs is destination BBS (again without any - number) [OPTIONAL]
        ---> If @BBS part is omitted then if the station has entered
        a Home BBS (NH command) that BBS will be used. Otherwise the
        to station callsign will also be used as the @BBS.
        Example: S W1XXX @W0YYY

        You will next be asked for a title for the message.
        After this you type the message, keeping all lines less than 80
        characters. When you are done with the message type ^Z or /EX  on 
        a new line.

        Use SB to send bulletins, ST to send traffic, etc. All messages
        sent  to  a specific callsign will be treated as if you  used  SP 
        (send
        private).  To  make messages to a specific callsign  readable  by 
        everyone use SB instead of just S!
        The U command gives the current users of the bbs plus the  number 
        of active messages and users and what they are doing.


                                   31




        The  V  command gives the version of this software and  date  and 
        time MSYS was started.

        The What command lists the available files for downloading. The
        formats:

             W    - Lists all files with dates & sizes
             W  (Directory)  - Lists all files in  a  subdirectory  under 
        files
             WN   - Lists recently added files with short descriptions of 
        the files

        The X command can be used to set or reset Expert status and  also 
        to  set  the  number of lines sent before  pausing  during  an  R 
        command.  If no argument is given, X simply toggles and  displays 
        the  new  Expert status. When Expert status is set,  the  initial 
        connect messages are replaced by a compatibility identifier  line 
        (currently [MBL313]) and the command prompt is simply >.

        If a number is given after X, this is the number of lines to
        display  for  a  R  command  before  asking  More?  To   continue 
        displaying  the current message when More? is sent press  return. 
        To  abort the message, type N and then return. This facility  has 
        been  added  to prevent a long message from  scrolling  off  your 
        screen faster than you can read it.
        Experiment with different values until you find one that  pleases 
        you.  To not use this facility, set the number of lines to  zero. 
        Examples:
        X 20  (pause after every 20 lines)  X 0  (don't pause ever)
        When you get More? in R cmd output(as a result of using X cmd  to 
        set  lines between pauses) you can  type C for  continue  without 
        any more stops.
             Putting * at the beginning of a line makes it a comment.
        It also suppresses the next command prompt (but the system will
        be waiting for another command). * is useful to answer the  SYSOP 
        if you get a MESSAGE FROM SYSOP ...





















                                   32




                                 DATABASE HELP #
                    (c)  Copyright 1989 by HUB COMPUTERS, INC


           Commands related to database manipulation available on MSY


             I'm not sure of just what to do with them, but I have added
        two new facilities to MSYS that may be used for a variety of
        purposes.  MSYS can now allow BBS users to input information  and 
        search  for  information in simple data bases. The names  of  the 
        databases  are  DATABASE.0  thru DATABASE.999.  These  files  are 
        located in the normal FILES directory, which can be accessed by
        the D command (download) on the BBS.
             These files can also be searched by the new G command on the 
        BBS.  To  use  this  command you enter the  command  G  (with  no 
        operands).  You  will  then be asked for the  file  you  want  to 
        search.  Simply  pressing  return  at  this  point  will   select 
        DATABASE.0 by default. You are then asked for the search  string. 
        This is a set of characters that when found in lines of the  file 
        cause  those  lines to be displayed. Case is ignored  during  the 
        search. If a selected line ends with \ then the following line(s) 
        are also selected for
        display.
             Data  is  entered into a data base by sending a  message  to 
        MSYS  with  DBADD in the title. The text of the message  will  be 
        added to the indicated database (DATABASE.0) by default. A header 
        line  is also inserted in the data base telling the station  that 
        made  the  entry,  along with the date and time.  Here  are  some 
        examples:

        SP MSYS                  {this is a S command issued to the BBS}
        DBADD 3                  {the message title, DATABASE.3 to be used}
        wind damage mentor ohio \
        large tree down at 615 & 20 \
        reported by mentor pd \
        no injuries
        ^Z                       {normal way to end message}

        The text of this message would be added to database.3. Now if
        you search database 3 for either     wind damage   or  mentor
        for example, you would get to see these lines, along with any
        other lines that have    wind damage    or   mentor    in them.
        Example of using search command:
        G                        {BBS command to do search}
        File search routine      {Response from bbs}
        Enter file name (or just press return for DATABASE.0): database.3
        Enter search argument: Mentor
        {lines from message above displayed}
        >                        {BBS ready for next command}

        Another example:
        Assume a file had the following lines:
        Mary had a little lamb
        its fleece was white as snow, \


                                   33




        and every where that Mary went
        the lamb was sure to go.
        It followed her to school one day
        If you searched this for 'snow' you would get the following back:
        its fleece was white as snow, \
        and every where that Mary went

        Well thats a brief outline of what can be done. Its simple yet
        very flexible. Let me know of any applications you can think of
        for these facilities. Particular database numbers can be assigned
        to different uses. Formats for information can be suggested for
        each different database.













































                                   34




                           Forward File Description #
                    (c) Copyright 1988 by HUB COMPUTERS, INC.


             The   MSYS forward file (MSYSFWD.DEF) is an ASCII file  that  
        can  be  prepared with any program editor. The file  consists  of  
        groups  of  lines separated by a line beginning with at least   3  
        dashes.  Each group of lines specifies what should be sent  to  a 
        given  BBS along with other information.

             The first line has the following format:

        Position  Content
        --------  -------
        1         The letter F
        2         The port number to use (a single digit)
        3         A blank
        4 to N    Callsign of BBS (with SSID)
        optional:
        N+1       A blank
        N+2 to ?  Via list of digipeaters

        Examples:
        F0 W1XX V W2XX,W1XX-1
        F2 WA0XYZ-2

             When no nodes are being used, this first line is used as  if 
        it  were a connect command to the desired system. When a node  is 
        used, the Via digipeater list will have no effect.

             If  a node (KA Node or NET/ROM) is to be used, the next  set 
        of lines are a script of how to use the node(s). This script  may 
        be up to 25 lines long. Its format will be described below.

             Next comes a list of callsigns of BBS systems that should be 
        forwarded  to  the  system  given on  the  first  line  (the  one  
        beginning with F). There is one call per line. No SSID should  be 
        given. The callsign of the system given on the first line  should 
        normally be given in this list.
        Example forward file that doesn't use any nodes:

        F0 W1XX
        W1XX 
        W2ABC
        W2XXX
        ----------
        F0 W1XX V W1XYZ
        W1XX
        W2ABC
        W2XXX
        ---------
        F1 W1XX V K1XXX,W1XXX
        W1XX
        W2ABC
        W2XXX


                                   35




        --------------
        F0 W8XXX-12
        W8XXX
        WA8XXX
        K7XXX
        ---

        Note: Here we try three different paths to connect to W1XX. If we 
        get  the messages forwarded the first way the  other  connections 
        will not be attempted. 

        F0 W1XX
        !01-04,12,21-23   This  will forward during  the  times  indicated 
        W1XX               (Use of this line is optional.)
        W2ABC                                                                               
        W2XXX     
        ----------

        In the list of callsigns given indicating what BBS's msgs
        can  be forwarded to a particular BBS if a second entry is  typed 
        on  the  line  then the second entry must match some  part  of  a 
        message title to allow it to be forwarded. For example, 

        F1 W1XX
        ARRL DX
        ----------

        @ARRL will be forwarded only if DX appears in their
        title. Case of letters is ignored in the comparison.

        You can use * in the forward file. If you have NTS* then
        all msgs with NTS as the first 3 characters of the @BBS will
        be forwarded. For example:

        F1 W1XX
        NTS*
        ----------

        * used alone is treated specially. Only messages
        that have been on the BBS for more than about 2 days will be
        forwarded. This gives time for them to be forwarded by other
        specified connections. 

        IMPORTANT  NOTE:  In the forwarding file, use of *  for  the  BBS 
        names  cannot be the first call and the first bbs in the list  of 
        bbs's that can be forwarded to thru the given bbs MUST begin with 
        a letter. Thus

        F0 WA8BXN
        *              won't work
        WA8BXN
        -----------
        F0 WA8BXN
        44*            won't work
        WA8BXN


                                   36




        -----------
        F0 WA8BXN
        WA8BXN         will work
        *
        44*
        -----------

        Node Scripts:

        The script consists of several sets of lines. The first line 
        begins  with  @  followed  immediately  by  the  call  (and   Via 
        digipeater  list if needed) of the node to initially connect  to. 
        The port that will be used is taken from the digit after the F on 
        the first card in the group. 
        If the connection is established to the node, the  following 
        sets  of  lines are used to talk to the first node  and  possibly 
        other nodes called through it.
        Each  set of lines for a given node begins with a line  that 
        has  a  period in position one. The following characters  on  the 
        line are sent to the node as a command.
        The  next line in the set is optional and if used has  #  in 
        the  first position. Following this is the number of  seconds  to 
        wait  before  abandoning use of this node. If this  line  is  not 
        given then 60 seconds will be assumed.
        The  next  line is required and begins with + in  the  first 
        position.  The  following characters are what is  looked  for  in 
        lines  that  come from the node to indicate that  connection  has 
        been  established  to  the station called (another  node  or  the 
        desired BBS). An exact match to the characters given on the  line 
        (including  case) must be found somewhere in a line  received  to 
        continue.
        Next can optionally come up to two lines beginning with ? in 
        the  first  position. These cards contain strings  of  characters 
        that  if found anywhere in a line that comes from the  node  that 
        the connection was not made. 
        Thus  after we issue the connect command (given on the  line 
        beginning with .) one of three things can happen: a line from the 
        node  that matches the +string is found and we continue with  the 
        script or talk to the BBS, a line from the node matches a ?string 
        which  means we give up on making the connection, or  a  time-out 
        occurs waiting for a match which again means we will give up  the 
        connection. 

        Example script:

        @ANOD          (issue connect command to ANOD)
        #25            (time out after 25 seconds if no match)
        +MADE          (if MADE comes from node, continue)
        ?BUSY          (if BUSY comes from node, abandon attempt)
        ?RETRIED       (if RETRIED comes from node, abandon attempt)

        These  strings  are useful for KA Nodes. For a NET/ROM  node  the 
        following would be useful:
        +to
        ?Failure


                                   37




        ?Busy
        Here is another example of a complete forward file:

        F1 W8XXX
        W8XXX
        W5XYZ
        ---------
        F0 W4XYZ
        @W7XXX
        +to
        ?Busy
        ?Failure
        @W9XXX
        #120
        +MADE
        ?RETRIED
        ?BUSY
        W4XYZ
        W4XXX
        -------
        F1 W9XXX-2 VIA K9XXX-3,KA9XXX
        W9XXX
        W1XXX
        W3XXX
        K0XXX
        ----------

        The file MSYSBBSB.DAT

        This   file   contains  a  set  of  bit   position   numbers 
        and corresponding BBS calls to which $ BID  messages 
        will be sent. The format of the records is MAX BIT# IS 32 
        Bit# Callsign

        An example file content is:
        25 WB8JUI
        26 KB8CI
        27 WA8YWH
        28 KQ8M
        29 KB3X


        Info:

        (MSYSFWD.DEF): If you put a line beginning with
        $  and followed by a file name (where BBS callsigns normally  go) 
        the  given  file will be read at that point as  more  BBS  calls. 
        Example

        F0 WA8BXN
        WA8BXN
        $BXN.DAT
        ARRL
        --------



                                   38




        In this example, the contents of BXN.DAT will be used for more
        calls  that  can  be  forwarded thru WA8BXN.  Due  to  the  extra 
        overhead  of opening, reading, and closing the file, this  should 
        only be used for more than just a few call signs.

        Hierarchical forwarding:

        This  means that send commands like S WA8BXN @  WA8BXN.OH.NA  are 
        supported.  Forwarding is attempted first using WA8BXN. If  there 
        is no entry for WA8BXN then it is treated as if it was S WA8BXN @ 
        OH.  If no entry is found for OH in the forwarding file, then  it 
        is  treated  as S WA8BXN @ NA. If that fails, the msg  won't  get 
        forwarded!

        Merge: (MUST DO THIS IN ORDER TO FORWARD MAIL)

        This  command  reads  MSYSFWD.DEF  and  copies  it  to  MSYS.FWD, 
        expanding any include files ($filename). A file is also produced,
        MSYS.BBS that is a sorted list of all possible BBS's that can be
        forwarded to (including things like ARRL, 44*, etc). This command
        is for 2 reasons: if there were any include files in the MSYS.FWD 
        files  they  did  not get read when a pf  command  was  used  and 
        secondly, the new file is needed for hierarchical forwarding.
        The leftmost part of the hierarchical route only is used for
        forwarding and the contents of the file is  needed for efficient
        processing.  Any  changes you make to your forward file  must  be 
        done to MSYSFWD.DEF followed by use of the MERge command (IN  THE 
        BBS).

        Call/@BBS replacement facility:

        Create a file called MSYS.REP In it place lines with the
        following format

        OLDCALL OLD@BBS    NEWCALL NEW@BBS

        For example:

        ALL  ALLONT   ALL  NEOH        (messages  to  ALL@ALLONT   become 
        ALL@NEOH)
        44* NTSOH   @1  ---        (messages to 44*@NTSOH become original
                                        tocall@ ---)
        NTS*  * @2 @1               (messages coming in to  NTS  anything 
        get
                                    tocall and @bbs swapped)

        ***  IMPORTANT  *** There can be no more that 100 lines  in  this 
        file!  The algorithm goes like this: When a message comes  in,  a 
        check is made comparing the to call and @bbs of the msg with  the 
        first two fields of the records in MSYS.REP. If a match is  found 
        (wild  cards are allowed in MSYS.REP) then the last 2 fields  are 
        used  to replace the tocall and @bbs of the message. @1 or @2  in 
        the last two fields in MSYS.REP have a special meaning. @1  means 
        the  original to call and @2 means the original @bbs.  Note  that 
        wildcards are not expanded in these last 2 fields.


                                   39




        To support this facility a new command is also added: REPlace.
        If an argument of L is specified, the current replacement list is
        displayed.  If  no  argument is given, the  current  contents  of 
        MSYS.REP  are read and stored in memory. (This is done when  MSYS 
        is  started  also).  Use the REP command after  you  have  edited 
        MSYS.REP to make the changes effective.

        REVERSE FORWARDING :

        MSYS  can respond with messages to a connected BBS when it  gives 
        F>.  To  use this facility, you must have a  directory  FWD  that 
        contains files of the form callsign.REV. These files contain  the 
        @BBS  values that can be reverse forwarded to the given  station. 
        So you may want to set up your forward file as follows:
        [file MSYSFWD.DEF]:
        F0 W8XYZ
        $fwd/w8xyz.rev
        --------
        F0 K8XXX
        $fwd/k8xxx.dat
        --------
        [file FWD\W8XYZ.REV]:
        W8XYZ
        ARRL
        [file FWD\K8XXX.DAT]
        K8XXX
        K9XYZ
        ARRL

        With these example files, reverse forwarding would be enabled for
        W8XYZ but not K8XXX. Recall that $ lines in the the forward file
        MSYSFWD.DEF  cause the given file to be included at  that  point. 
        Also  remember to be sure to use the MERge command  whenever  you 
        make  any changes to the forward files! Reverse forwarding  of  a 
        given  message is not possible until there has been at least  one 
        normal  forwarding  (either  forced  manually  with  the  FOrward 
        command  or  at  your forward time). The other  half  of  reverse 
        forwarding  (where MSYS would send F> when it is done  forwarding 
        messages  to a particular station) is not implemented. It  should 
        not  be  needed due to the multiconnect nature of  MSYS.  If  you 
        really need it, let me know and I will consider adding it.

        TCP/IP FORWARDING:

        TO forward to VE3GKM-4's TCP/IP mailbox the file would look  like 
        the folowing.

        F0 VE3GKM-4
        @VE3GKM-4
         .
        +NET
        VE3GKM
        (MORE @BBS CALLS)
        --------------- 



                                   40





        *** FORWARDING NOTES

        The MSYS.BBS file contains a number after each "BBS" that
        the system knows how to forward to. This is the ORing of all the
        BBS Masks that can be used to forward the particular @BBS. This
        is  used  to  determine  when bulletins have  been  sent  to  all 
        stations  that  should be getting them; when such a  bulletin  is 
        found,  it  gets its type changed from $ to # so then  it  is  no 
        longer considered for forwarding.

        BID:
                
        When a msg comes in to non-callsign without a bid a check is
        made with generated BIDS of msg#_callsign and callsign_msg#
        to eliminate duplicates.

        Messages addressed to other than a what looks like a callsign
        automatically get a BID generated for them. 

        Mail forwarded to BBSs identifying with either [MBL or [... -  $] 
        get 
        BID included in S command.

        If a message is sent to MSYS @ idcall then the
        text is scanned for a line with:

        ;;; forward thru callsign

        If one is found, then all unread mail for the originating station
        that  is  on  the  bbs gets its @BBS  changed  to  the  specified 
        callsign. This includes the msg to MSYS which gets changed to  be 
        to the originating station @ specified callsign. The title of the 
        msg is changed to indicate the number of msgs that were  changed. 
        All changed are forced to be private. This command allows you  or 
        your  users to get any traffic for them on your bbs when the  msg 
        is  received  routed to another bbs (assuming your  system  knows 
        how  to  forward it there). Additional features in msgs  to  MSYS 
        will be added later.

        FORWARDING DISPLAY:

        As  each of the BBS's to which msgs can be forwarded  is  scanned 
        for  a given bbs you will see it. When a msg is  being  forwarded 
        you will see a line that gives its number and the to station  and 
        @bbs of the message. In parenthesis you will see the entry in the 
        forward  file  that is being used. Thus if  the  forwarding  file 
        contained

        F0 WA8BXN
        WA8BXN
        44*
        ---------
        and there was a message for K8ZZZ@44123 being forwarded you
        would see something like Fwding msg # 123 K8ZZZ@44123(44*).


                                   41





        DROPING @BBS:

        Messages that arrive with @BBS of IDCALL get the @BBS field
        changed to  ---. This makes them distinctive 

        FTImes if time is negative number such as -5  then  you 
        will forward every 5 minutes

        *** There can only be up to 300 different bbs names in the 
            forwarding file

        ****  BE SURE TO INCLUDE MSYS in your forward files for all other
        MSYS stations you forward to so I can send bulletins about MSYS
        to all of you. The list of MSYS operators keeps growing!  ****










































                                   42





                         MSYS General information file #
                    (c) Copyright 1989 by HUB COMPUTERS, INC.


        *** MEMORY MANAGEMENT:

        Buffer space for logical channels is allocated when the
        channel is allocated (and released when the channel is released)
        This will cause the MEM command to show more available memory.
        Its is little deceptive though because when all the channels
        are in use the same amount of memory will be used as before.

        *** Remote SYSOP:

        \Sysop command:

        It  gets you into remote sysop mode which allows you to use  most 
        of the sysop commands thru  the bbs.  The  command  must be typed 
        exactly  as  shown:  backslash, Capital S and lower case ysop and 
        then return.You will then get a line like
         
        Usage stats: Users=4 Msgs rcvd=10 Msgs sent=5 Max=8

        To this you must reply (there will be no prompt) four  characters 
        corresponding  to the numbers typed in order of characters  found 
        in  the file MSYS.RMT (case is important). For example,  if  your 
        MSYS.RMT file contained MSYS is the greatest!
        then  you  would type <space> e i t which are  the  corresponding 
        characters  (the first character is numbered 0). Thus  you  would 
        type eit  (Don't forget to count the spaces)
        You should now get a prompt cmd:

        To get a list of available commands, type h. To exit, type q  and 
        you  will get back to the normal bbs command prompt. Most of  the 
        commands  available  duplicate  those  found  normally  as  sysop 
        commands.  An added command, who, gives a list of who is  on  the 
        system and is the same as the new U command in the bbs.

        *** MSYS.DO:

        A  command  file may contain the same things you  could  normally 
        type as commands. To execute a command file, type DO followed  by 
        the command file name.

        Example:   DO cmds.dat

        When the system starts it automatically tries to DO a command
        file called MSYS.DO.

        *** MONxx:

        MONCC ON/OFF - enables/disables monitoring of TCP/IP packets
        MONCF ON/OFF - enables/disables monitoring of NETROM packets



                                   43





        *** LINKED:

        A line of the form *** LINKED to callsign now recognized
        as  a  connection by the given callsign. This  occurs  with  some 
        versions of RLI systems when a user uses the C command on the RLI 
        system to connect to the MSYS BBS.

        *** LINKED to callsign requires sysop verification if sysop call
        is used

        *** KEYBOARD:

        When someone connects to your keyboard answer call you will
        get two musical tune to alert you to the connect.  
        --- Any stations connecting to your keyboard call when you are 
        already connected to another station will get a busy. The actual 
        number of connects allowed before busy is given by the new sysop 
        command MCon. MCon 1, for example, only allows an incoming call 
        to the keyboard to be answered if there are no other keyboard 
        connections. MCon 0 prevents all incoming keyboard requests (they 
        get busy). MCon N will allow N connections to the keyboard until 
        busy is returned.
        --- When you type past column 72 you will get a beep for each
        character. Keep those lines less than 80 characters!

        *** Packet size:

        Data in packets is limited to 256 bytes. Larger amounts
        of data in a single packet will be discarded without causing the
        system to crash.

        *** STACK requirement:
                
        The stack space needed by the forward process has increased. 
        The  following  line  can be put in MSYS.OPT  (This  may  not  be 
        necessary):

        STACK FORWARD 8000

        A  smaller value (maybe 7000) might work. Try it if you want.  If 
        the system randomly crashed, make it 8000.
         
        *** SENDME:

        SENDME command  Usage: sendme message #
        This command will send you a copy of the given message number, if 
        you are in the forward file. Example: sendme 5
        Note that you have to spell out sendme completely!
             
        *** S:
         
        The S command has been modified to make all messages private 
        that  do not have a type indicated in the S command (such as  SB) 
        or are addressed to non-callsigns (such as all).


                                   44




        Modifications  have been made to the R command to list  path 
        information  with  R: lines using either  @:bbscall  or  msg#@bbs 
        format.
        *** BBS Commands:

        ST Command will not add bid to messages.

        Download requires that the first character of the file name be
                alphanumeric (no more ..)

        *** @BBS:

        Automatic generation of @BBS field for S command in BBS: If the
        S command contains an @BBS entry it is left untouched. If there
        is no @BBS as a parameter for the S command, the the following
        happens. If the to station is found in the user file then the
        home bbs field is made the @BBS field. If the to station is
        not a known user then the to station callsign is placed in the
        @BBS field.

        Any messages entered into the system with no @BBS that don't get
        a @BBS from the user file will have ==== for the @BBS.
        Only messages with second type character of N will cause the
        user file to be searched for @BBS now. Thus bulletins will never
        get their to call sign (typically ALL) looked up in the user 
        file.

        *** MSYSTNC.#:

        If you use any tnc set up files be warned that the program waits
        1 sec after each line from the file is sent to the tnc to give it
        time to think about it.

        *** MAIL BEACON:

        Messages to your IDCALL and to SYSOP are not displayed in the
        MAIL FOR beacon. You will see them on the screen.

        *** LOG:

        Msgs sent, forwarded, and killed get logged to MSYS.LOG.

        *** LOCKUPS:

        If the system hangs an attempt is made to reboot. Thus you should
        make sure you don't have a diskette in A: and that you have
        an appropriate autoexec file set up.

        *** WHAT FILES:

        W does a directory listing of the FILES directory. You can also 
        now give a sub-directory after W to get a list of files in that 
        subdirectory of FILES. The directory list provided includes the 
        size of the files listed.



                                   45





        *** CHANNEL NUMBERS:

        The channel numbers use a rotational assignment rather then
        always starting from 0 

        *** USER BIT SETTINGS:

        $04 - Disconnect immediately 
        $08 - Limited BBS

        When the BBS is in limited mode and the H cmd is used, the file
        printed now is HELP/HLIMITED.HLP in place of HELP/HELP.HLP

        *** #:

        Command lines beginning with # on the BBS are  ignored (they
        sometimes come from KA Nodes).


        *** MAX CHANNALES AND PORTS :

        Maximum for MAXCHANS is  50   (MSYS.OPT)

        Maximum number of ports is  6
            
        *** END OF LINE BELLS

        When you type past column 72 you will get a beep for each
        character. Keep those lines less than 80 characters!



























                                   46





                     CHKMAIL/LFA/MRESTORE/MAILSIZE/BBSLIST #
                    (c) Copyright 1989 by HUB COMPUTERS, INC.

        *** CHKMAIL:  

        When MSYS.MSG gets messed up you run CHKMAIL 
        Chkmail will search for errors in the mail file.
        If run with -d option chkmail will delete all errors in the  mail 
        file
        Example:

        CHKMAIL -D    THIS WOULD FIND AND DELETE ALL DAMAGED MAIL FILES

        I have chkmail run before msys starts
        by putting it in a batch file I use to start MSYS.

        *** LOG FILE ANALYZER:

        A new program LFA is included that prints summary information
        of  usage using your MSYS.LOG file. At the end it also  prints  a 
        list  of  message numbers that were created as messages  but  not 
        deleted. These messages should normally be active messages on the 
        BBS. If not they were somehow lost and you might want to get them 
        back   using  MRESTORE.  Note  that  this  list  uses  only   the 
        information found in MSYS.LOG.

        *** MAILSIZE.EXE:

        Just  run  mailsize  to change the  maximum  number  of  messages 
        (either  up or down now). Every message slot allocated  cost  138 
        bytes.   I  would  recommend staying at no  more  than  400,  and 
        normally  try to keep active message count below 200.   The  more 
        active mesages there are,  the slower the system will run.

        *** MRESTORE.EXE:

        Due  to  system crashes sometimes causing the  loss  of  messages 
        several  new features and a program have been added to  the  MSYS 
        system.  Note  that  the  program CHKMAIL does  do  what  it  was 
        intended to do, namely give a MSYS.MSG file that does not contain 
        any errors. Unfortunately sometimes several messages that were in 
        the  system  are  deleted if MSYS.MSG is  messed  up  enough.  To 
        recover  such messages, and others that were deleted and need  to 
        be  recalled, MSYS will now make a separate copy of each  message 
        as  it is sent to the system if the directory MAIL.BAK exists  in 
        the default directory (the same place MAIL and FILES are  found). 
        To  make  this directory just type MD MAIL.BAK (it  will  work!). 
        Messages  stored  in this directory are not  accessible  directly 
        from the BBS. You can type them, etc., as normal files (they have 
        the  same  names  as  messages  in  the  MAIL  directory,  namely 
        MSGnnn.dat).  They are not quite the same format as the files  in 
        the MAIL directory as they contain additional information that is 
        normally found in the file MSYS.MSG. You can type them and get to 
        see the header information. To recover a message no longer on the 


                                   47




        BBS  you must stop MSYS and run the program MRESTORE. It is  menu 
        oriented  and should be self explanatory. Since all messages  are 
        saved in the directory MAIL.BAK if it exists you can look at  any 
        message that passed through your system. But be warned that files 
        are  not automatically deleted from this directory. Thus it  will 
        get  larger  and  larger. You  should  periodically  archive  the 
        contents  of  this directory and delete the files. If  you  don't 
        want  these files saved at all, simply don't create the  MAIL.BAK 
        directory.

        *** BBSLIST.EXE

        This program scans messages headers and compiles a list of bbs
        calls, qth's and zip codes.
        To use this program type BBSLIST [directory name]
        where directory name is where the messages are to be scaned.
        This produces the file bbslist.dat








































                                   48





                             EDITVIEW (ED Command) #
                    (c) Copyright 1989 by HUB COMPUTERS, INC.

             The  ED command used from the MSYS command mode can be  used 
        to edit small text files. The file is limited to records each  80 
        bytes  or less in length. By default up to 200 records may be  in 
        the  file. This can be modified by giving the maximum  number  of 
        lines  after  the file name. The intent of this editor is  to  do 
        little  things  without having to take down the system to  run  a 
        more powerful editor. These might include editing message  texts, 
        the forward file, etc.
             ED is a full window editor (it adjusts its operation to fill 
        the  window it is run in). It must be run in a window that is  80 
        characters wide. Thus using the default window definitions it can 
        be  run  in  the normal command window (0) or  you  can  use  the 
        CMdwindow  command to first go to window 4 (the one you get  when 
        you press F4) and then use the ED command. You will then be using 
        the entire screen for your editing.
             ED  is  pretty much a what you see is what you  get  editor. 
        There  are two modes of operation. When you start the editor  you 
        are in full screen or edit mode in which changes you make to  the 
        screen are also made to the file. In this mode you get a line  at 
        the  bottom  of  the window that gives such  information  as  the 
        current line number and the name of the file being edited.
             The other mode is command mode in which you give commands to 
        be  done  by the editor. To enter command mode press  the  Escape 
        key.  The  bottom line will change to Edit Cmd:  and  await  your 
        command. The command you type will appear on this bottom line. To 
        get  a  list  of available commands type  Help.  You  should  see 
        something that looks like the following:

        Commands
             Find - locates given string. Example:  F wa8bxn
                    Notes: Not case sensitive. F10 from edit mode
                    is find same string again.
             Insert - puts blank line at beginning of file
             QUIT - Abandons edit
             SAVE - Saves file and exits
             DELete - Delete specified # of lines from file beginning
                    with current line
             Return key in edit mode with insert on inserts blank lines

        Press a key to return to edit 

             Use  of  the keypad to move around in the file  is  what  is 
        expected  of the labeled keys, with the  following  enhancements. 
        If you are somewhere in a line and you press the Home key you  go 
        to  the  beginning  of  the current line.  If  you  are  are  the 
        beginning  of  the  current line and press Home  you  go  to  the 
        beginning  of  the  screen. If you are at the  beginning  of  the 
        screen, pressing Home takes you to the beginning of the file. 





                                   49





                             EDITFILE (EF Command) #
                    (c) Copyright 1989 by HUB COMPUTERS, INC.

             The  EF command used from the MSYS command mode can be  used 
        to edit small text files. The file is limited to records each  80 
        bytes  or less in length. By default up to 200 records may be  in 
        the  file. This can be modified by giving the maximum  number  of 
        lines  after  the file name. The intent of this editor is  to  do 
        little  things  without having to take down the system to  run  a 
        more powerful editor. These might include editing message  texts, 
        the forward file, etc.
             This  isn't  a full screen editor but rather a  line  editor 
        that  was influenced its design by the UNIX    editor. Plain  and 
        simple,  nothing fancy is found in it. To begin editing, use  the 
        command  EF filename when you have the cmd: prompt. The  filename 
        can  contain  drive and path information. If the  file  does  not 
        exist you will be given the option to create one by that name. 
             To create a new file this way, use the Append command.  Type 
        the  lines of the new file and then a line with a period  at  the 
        beginning  to  exit append mode. The use the commands  Write  and 
        Quit (each followed by the return key) and you have created a new 
        file. All of the commands can be shortened to the first letter of 
        the  command,  except for the DElete command  which  requires  at 
        least the first two letters.

             Here is information about the commands:
        #   (i.e.,  a line number) makes that line the current  line  and 
            also displays it

        + # Makes the current line # more than it is now. If # is omitted 
            then the current line is incremented by one. 

        - # Same as + # except current line number is incremented. 


        <ESCAPE> Using the Escape key followed by the Return key abandons 
            edit  with no changes made to the file (unless you  used  the 
            Write command yourself).

        <RETURN> Pressing the Return key alone displays the next line and 
            makes it the current line.

        Append  enters input mode, placing the following lines  of  input 
            AFTER  the  current  line. A line  beginning  with  a  period     
            terminates append mode.

        Bottom makes the last line the current line and displays it.

        Change can be used to replace part of the current line. The first 
            non-blank character after the command is the quote character. 
            The  operands  are quote-character  string-to-replace  quote-
            character replacement-string quote-character. For example,
                 C /YXZ/abc/
            would  replace XYZ in the current line with abc. The line  is 


                                   50




            printed after it is displayed.
        DElete  can  be used to delete the current line. If a  number  is 
            specified as an operand, it is the number of lines to  delete 
            beginning with the current line.

        Down  moves the current line down the number of  lines  specified 
            (or 1 if none is specified). 

        Find uses the first non-blank character after the command word as 
            the  beginning of the search string. The search is  from  the 
            current  line  on in the file. Case is NOT  important.  If  a 
            match  is found the line is displayed and that  line  becomes 
            the  current  line.  If no match is found  the  current  line 
            remains unchanged.

        Help displays the list of commands.

        Insert is like Append except that the new lines are placed BEFORE 
            the current line.

        Near displays the contents of the file 5 lines before and 4 lines 
            after the current line which remains unchanged.

        Print with no operands displays the current line. Give 1  operand 
            it  displays  the  line with that number.  Given  2  operands 
            (separated with a blank or comma) it displays from the  first 
            to  the second line number. The current line  number  remains 
            unchanged.

        Quit is used to exit the editor after the file has been written.

        Top  makes  the  first line (numbered 0)  the  current  line  and 
            displays it.

        Up decrements the current line number by the number given or 1.

        View  displays the current line and the 9 lines that  follow  it. 
            The current line remains unchanged.

        Write causes the file to be written to disk with any changes that 
            have been made.

        ^F  is used to search again for the same search string give  with 
            last use of Find.

        To start the editor, type EFile filepathname [# of lines max]. 
        Examples:
        ef msys.fwd 250
        ef mail/msg25.dat
        efile a:f1.c







                                   51





                          HOUSECLEANING (HC command) # 
                    (c) Copyright 1989 By HUB COMPUTERS, INC                       

        MSYS.HCL

        You create a file called msys.hcl. In it you put lines describing
        classes  of  messages  you want to eradicate.  Each  line  should 
        contain one or more of the following keywords:

        AT= TO= FROM= AGE= TITLE= TYPE= KEEP= SYSOP=

        So for example:

        AT=ARRL AGE=30
        would delete all messages with @BBS of ARRL that are over 30 days 
        old.  If  specified,  the values of AT TO  and  FROM  must  match 
        exactly for a message to be deleted. TITLE and TYPE if  specified 
        must  match  some  part of  their  corresponding  message  header 
        fields; case is ignored.

        KEEP can be used to specify a number of msgs that match the other
        values given that should be saved anyway.
         
        Example: TO=ALL AT=ARRL TITLE=PFB KEEP=2
        Would keep the newest two messages to ALL@ARRL with PFB somewhere 
        in their title. The value of title given cannot contain blanks.

        SYSOP=Y  has to be specified in any line that you want to  delete 
        messages that are to the idcall of the bbs.
        Thus  to  delete all read messages (includeing one  to  you)  you 
        could  have  a line: TYPE=PY SYSOP=Y The following  line  deletes 
        read messages, except those to you: TYPE=PY

        The  effects of these lines can be far reaching. For example,  if 
        you put in the line: KEEP=5
        Then it will delete all but the 5 newest messages!
        All this action takes place when you type HClean NOW
        or  at a time specified as a numeric parameter to HClean. HC  120 
        would cause it to happen at 02:00  (number given is minutes after 
        00:00 [midnight] to begin housecleaning). 

        msys.hcl file as an example:  
        at=arrl age=21
        at=okipn age=10
        at=panet age=3 type=#
        at=alloh age=10 type=#
        at=neoh age=10 type=#
        at=allbbs age=7 type=#
        at=rlibbs age=7 type=#
        at=amsat age=7 type=#
        at=midnet age=3 type=#
        at=usnet age=3 type=#
        at=wpab age=3 type=#
        at=arrl title=pfb keep=1 type=#


                                   52




        at=arrl title=dx keep=1 type=#
        at=arrl title=keplerian keep=1 type=#
        type=# title=sale age=2
        type=# title=need age=3
        type=# age=35
        type=py keep=1
        type=pf keep=2
        type=tn age=21
        type=pn age=60
        to=sysop age=7 type=#















































                                   53





                       Sysop commands related to TCP/IP #
                    (c) Copyright 1989 by HUB COMPUTERS, INC.

        MYIpaddr takes four integers in the range 0 to 255. It sets the
        IP address that the system will respond to. Example: MYI 44 70  4 
        6  If  MYIpaddress is not specified, or set to  all  zeroes,  the 
        TCP/IP support will be inactive.

        MYTcpip  takes  a  callsign (with SSID) that will  be  used  when 
        sending arp and TCP/IP frames. It can be the same as the ID  call 
        in most cases.

        TElnet  takes  an  IP  address  and  optional  server  number  as 
        parameters.  A symbolic IP address may given to be looked  up  in 
        the file MSYSHOST.NET. Default server is 23. This command is used 
        to  establish  keyboard  to keyboard  connection  with  a  TCP/IP 
        station.
        Examples:  TE [44.70.4.10]
                   te hsp             (hsp would have to be defined in
                                        MSYSHOST.NET)

        TElnet operates much like C# normally used to connect to AX.25
        stations. ^Cd is used to disconnect.

        TPorts  takes  a port mask value as an argument. This  number  is 
        used the same way as in in the other similar commands: each port
        corresponds to a port (port 0 is the rightmost bit) and when the
        bit is set to 1 for a given port that port is available for
        TCP/IP use (particularly ARP broadcasts).

        ARP used without an argument lists the known callsign/IP address
        correspondence   determined  by  TElnet  connects.  An   optional 
        argument, CLEAR, may be used to erase all of the ARP entries.

        FTP  takes  a  host-id as an argument (it can  be  either  an  IP 
        address  in  the square brackets or a symbolic  IP  address).  It 
        establishes  a  connection  to the FTP server  of  the  specified 
        system. FTP is the File Transfer Protocol used in TCP/IP.

        SMTP  allows  local access to the SMTP server  (mainly  for  test 
        purposes).

        Note: The following servers are currently implemented in MSYS:
                7       Echo
                9       Discard
                21      File Transfer Protocol
                23      Telnet
                25      Simple Mail Transfer Protocol


        *** Files related to TCP/IP

        MSYSHOST.NET  This  is an ascii file you create  with  an  editor 
        (such as the MSYS ef command). Each line in the file begins  with 


                                   54




        an  IP  address  that includes the periods  but  not  the  square 
        brackets around it.
        Following this there is at least one space and/or tab  character, 
        then  the list of symbolic names (or aliases, or nicknames,  what 
        ever  you want to call them). You may place comments on the  line 
        by  beginning the comments with a pound sign (#).  Example  entry 
        line for this file: 77.70.4.6 bxn mike wa8bxn # kirtland, oh
        This line would allow "bxn" "mike" or "wa8bxn" to be used as
        arguments  in the TElnet and FTP commands. Note that WA8BXN  here 
        just  happens to look like a callsign. The actual  callsign  (and 
        SSID)  associated with a particular IP address is  determined  by 
        ARP  (address  resolution protocol)  broadcasts.  These  symbolic 
        names  you  define in this file simply relieve you of  having  to 
        remember (and type) complete IP addresses. Nothing more,  nothing 
        less!

        MSYSPASS.DAT This file contains the user names and passwords for
        FTP users. Each line contains 3 or 4 items:
        username password access directory
        Username  is  the  name the user will use to log in.  It  can  be 
        anything  for  a  given  user. It  could  be  their  callsign  or 
        something  else. The password can also be anything. If you put  * 
        as the password in the file for a particular, any password  given 
        by  the  user  will be accepted. The third entry  on  each  line, 
        access, is a number that says how much access the user will  have 
        to  your  system: 1 means can only read files, 3 means  read  and 
        write  (but  not  replace or delete) and  7  means  read,  write, 
        replace  and delete. You shouldn't set 7 for any user  since  the 
        passwords  given by a user can be monitored by others.  The  last 
        item which should always be given is the root directory that  the 
        user  will have. They may never go closer to the real  root  than 
        what you give here. Here are some
        examples:
        anonymous * 1 files     --- this allows user anonymous to read
                                    any  files in MSYS/FILES and  any  of 
                                    its subdirectories. Any password  can 
                                    be  given  for this  user.  Anonymous 
                                    with   *  for  the  password  is   an 
                                    expected "standard" entry for  TCP/IP 
                                    systems  to  give access  to  totally 
                                    public files. Include it in your
                                    system.
        apple runtime 3         --- This allows user apple (who must give
                                    password  runtime) read/write  access 
                                    to   your   entire   disk    (DEFAULT 
                                    DIRECTORY IS THE REAL ROOT DIRECTORY!)

        *** USER ACCESS NOTE
        Access level chart

                Level 1: CD DIR GET PWD QUIT
                Level 3: PUT MKDIR
                Level 7: PUT (to replace existing file) DELE RMDIR

        If you are going to allow level 7 access (ie, can do everything)


                                   55




        I would suggest you also assign a directory that doesn't allow
        access to any needed files. For example, you might set up the
        following entry in the MSYSPASS.DAT file:
        WA8BXN MIKE 7 /MSYS/FILES/WA8BXN

        You will have to create a directory WA8BXN in the files directory.
        Now stations can log in with WA8BXN MIKE and do anything in
        /MSYS/FILES/WA8BXN and any directories found in this directory.
        If you set up
        ANONYMOUS * 1 /MSYS/FILES
        then the user ANONYMOUS can read anything put in the WA8BXN
        subdirectory of FILES (as well as in FILES itself) but not
        write or otherwise change anything. The rest of your files
        should be pretty well protected.

        *** FTP COMMANDS

        When you use the FTP command to connect to another system
        you can type HELP to get a list of the supported commands.

        They currently include:

                CD dirname  To move around in the directory structure
                CD          with no arguments gives the current directory
                DELE filename  To delete given file
                DIR filespec gives a directory listing
                GET filename   downloads a the given file
                MKDIR       makes a directory
                PUT filename   uploads the given file
                PWD         gives the current directory
                QUIT        disconnects
                RMDIR dirname  removes the given directory

























                                   56





                             Samples of MSYS files #
                    (c) Copyright 1989 by HUB COMPUTERS, INC.

        *** MSYS.OPT

        PORT 0 AT $3F8 INT 4 SPEED 4800 NAME  145.090
        PORT 1 SUBPORT 1 OF PORT 0 NAME 220.52
        PORT 2 AT $2f8 INT 3 SPEED 4800 NAME 145.030 RADIOSPEED 300 TNCTYPE 1
        NUMCHANS 10
        DIGI N8HTG-1 FROM 0 TO 1
        DIGI NT8V-1 FROM 0 TO 1
        DIGI N8HTG-1 FROM 1 TO 0
        DIGI NT8V-1 FROM 1 TO 0
        DIGI N8HTG-3 FROM 1 TO 2
        DIGI NT8V-3 FROM 1 TO 2
        DIGI N8HTG-3 FROM 2 TO 1
        DIGI NT8V-3 FROM 2 TO 1
        DIGI N8HTG-6 FROM 0 TO 2
        DIGI NT8V-6 FROM 0 TO 2
        DIGI N8HTG-6 FROM 2 TO 0
        DIGI NT8V-6 FROM 2 TO 0
        BBS ALIAS NT8V
        BBS CALL N8HTG
        ANSWER CALL N8HTG-13
        KANODE CALL N8HTG-8
        SYSOP NAME Lee
        SYSOP QTH PORT HURON, MI.
        SYSOP ZIP 48060
        ID CALL N8HTG
        FORWARD CALL N8HTG-15
        STACK FORWARD 8000
        FORWARD TIME 10
        ID EVERY 45
        MONITOR OUTGOING ON
        MONITOR IFRAMES ON
        MONITOR UFRAMES ON
        MONITOR BFRAMES ON
        AX25 RETRIES 10
        WINDOW 0 BACKGROUND 0
        WINDOW 5 BACKGROUND 0
        WINDOW 6 BACKGROUND 0
        WINDOW 2 BACKGROUND 0
        WINDOW 3 BACKGROUND 0
        WINDOW 5 FOREGROUND 10
        WINDOW 6 FOREGROUND 9
        WINDOW 2 FOREGROUND 12
        MAKE

        *** MSYS.DO

        WS 0 1 1 80 17
        WS 5 50 19 80 25
        WS 2 1 19 48 21
        WS 6 1 22 51 24


                                   57




        retries 5 5 5
        maxframes 4 4 4
        frack 15 15 15
        paclen 128 128 128
        BD 0 NM8X
        BT 0 N8HTG PBBS -- PORT HURON MI.
        BD 1 KV8G-3
        BT 1 N8HTG PBBS -- PORT HURON MI.
        MAKEP OFF
        TIMEZONE UTC
        MONST OFF
        MYI 44 102 0 75
        MYT N8HTG-4
        TP 2
        host xt.n8htg.ampr
        BELL ON

        *** MSYS.OTD

        <<< K-NODE = N8HTG-8 #### GATEWAY = N8HTG-1 145.03 <-> 145.09 >>>

        *** MSYSK.OTD 

        < Please try N8HTG PBBS ### N8HTG-1 Gateway 145.030 <-> 145.090 >

        *** MSYS.REP

        48060 NTSMI 48060 N8HTG
        48040 NTSMI 48040 N8HTG
        48001 NTSMI 48001 N8HTG
        48002 NTSMI 48002 N8HTG

        *** MSYS.RMT

        TEST PHRASE

        *** MSYSBBSB.DAT

        25 VE3WZL
        26 WA8BXN
        27 WB8I
        28 N8HTG
        29 VE3GYQ
        30 WA8OOH

        *** MSYSFWD.DEF

        F1 WA8BXN
        WA8BXN
        ----------
        F0 WB8I V NM8X-1
        WB8I
        ----------




                                   58





        *** MSYSHOST.NET

        # IP address         host name         alias      # comments
        #
        44.102.0.74         xt.nt8v.ampr       nt8v       #roy
        44.102.0.75         xt.n8htg.ampr      n8htg      #lee

        *** MSYSPASS.DAT

        guest * 3 public
        nt8v roy 3 
        n8htg lee 3
        k8dd hank 3 public

        *** MSYSTNC.1


        VHF OFF
        HB 300
        AWLEN 8
        PARITY 0
        CONMODE TRAN
        TRACE OFF
        HID OFF
        BE 0
        passall off
        RAWHDLC ON
        HP OFF
        PP ON
        KISS ON
        HOST ON
        host on
























                                   59





                                BIT PATTERN CHART #
                    (c) Copyright 1989 by HUB COMPUTERS, INC.

               To be used for DPorts, KPorts, MONPorts and TPorts

             [ PORT     3     2     1     0 ]       1=ON     0=OFF

        0               0     0     0     0  

        1               0     0     0     1      0-ON

        2               0     0     1     0      1-ON

        3               0     0     1     1      1,0-ON

        4               0     1     0     0      2-ON

        5               0     1     0     1      0,2-ON

        6               0     1     1     0      2,1-ON

        7               0     1     1     1      0,1,2-ON

        8               1     0     0     0      3-ON

        9               1     0     0     1      3,0-ON

        A               1     0     1     0      3,1-ON

        B               1     0     1     1      0,1,3-ON

        C               1     1     0     0      3,2-ON

        D               1     1     0     1      0,2,3-ON

        E               1     1     1     0      1,2,3-ON

        F               1     1     1     1      ALL ON


















                                   60





                              Frequent problems   #
                    (c) Copyright 1989 by HUB COMPUTERS, INC.


        --- The system will not forward.

        Make sure you executed the MERGE command.
        Without doing this the system will never forward.


        --- The system appears to work but nothing is on the screen.

        Make sure you set the diplay type correctly in the msys.opt file
        the command is WINDOW DISPLAY COLOR for color monitors and
        WINDOW DISPLAY MONOCHROME  for monochrome monitors.


        --- The system comes up and appears to hang.

        This may be caused by a non-existent com port, check the lines in 
        your msys.opt to make sure the port addresses are correct.


        --- The system boots after forwarding

        This may be caused by having too many entries in your forwarding 
        file remember you may only have up to 300 different bbs names in 
        your file.

        --- Performance hint:

        Don't let too many messages pile up in mail.bak <DIR> before  you 
        delete them (after archiving if you wish). Having too many  files 
        there makes S cmd on bbs very slow to respond with next >.






















                                   61





                     INFORMATION FOR USERS OF VERSION 1.01 #
                    (c) Copyright 1989 by HUB COMPUTERS, INC.

        MSYS 1.02 Update
        ****** IMPORTANT *****
        Beginning with this version, the forward hours line in the forward
        file MUST begin with !
        Old way                 New way
        F0 WA8BXN               F0 WA8BXN
        10-22                   !10-22
        WA8BXN                  WA8BXN
        -----                   ------
        LFA has been improved so that it should work with large amounts
        of input data. Try to keep input file size to periods of not
        more than 4000 messages having been passed!

        You should replace your current programs with the ones on this disk.

        A new program has been included that scans messages saved in mail.bak
        directory format. It produces a list of bbs headers seen in the msgs.
        File made is BBSLIST.DAT

        3-8-89
             A problem that has been around for a while has finally been
        identified. It deals with a bbs sending long messages to msys
        using a path that is marginal with frack>1. The symptom is that
        both stations go "wild" in flooding the channels with packets.
        Here is what happens: The sending station sends out multiple
        packets (call them 1 2 3 & 4). Due to noise msys does not receive
        packet #1 but does get 2 3 & 4. It sends out a REJ 1 for each
        of the packets received. For each of these 3 REJ packets the sending
        station resends all 4 packets again. If MSYS misses packet 1
        again each time (maybe its a long packet, or maybe the sending
        station has a txdelay that is marginal) then it sends out the
        REJ1 frames for all the other packets received (thats 9 REJ
        frames this time). The whole thing quickly snowballs into a mess.
        To hopefully avoid this situation, I have added the following
        command to MSYS:
        RESponsetime #   where # is the number of seconds to wait before
        sending out a response. This is the T2 timer value in thE ax.25
        spec. If you set RES to 0 it will work the old way, always sending
        out a response to each I frame received as soon as possible.
        With non-zero values for RES, the responses are held, the latest
        one replacing any one being held, until no I frames have been
        received for the time given. It then sends out its response. 

             Two other commands have also been added, both dealing with
        suspending the monitor function on the F2 screen (it takes a
        very significant amount of time to keep formatting all those
        packets displayed). The commands are:
        F2 #       # is the number of seconds to continue displaying
        monitored packets after F2 was last pressed. The default is 600
        seconds (10 minutes). Thus 10 minutes after you last press F2
        monitoring will be turned off until you press F2 again.


                                   62




        SUspendtrace #      Where # is the number of free bytes in the input
        buffers below which the monitoring is turned off. There is 1 buffer
        of 4096 bytes for each serial port (tnc). The amount free at any
        time is given by the STatus command. When the free space gets
        less than the SU value, F2 monitoring is turned off to allow
        things to get processed more quickly. Default value is 2000 bytes.
        Again, F2 displays take a lot of time and when the system gets
        behind it is a good idea to turn off the updating of the display.
        When the free space in all the buffers goes above the SU value
        tracing is turned back on (unless otherwise suspended). This
        function can be effectively disabled by setting SU to 0 and then
        it will work as before.













































                                   63





                                      INDEX

        Abort, 9, 14, 20, 32
        ACK, 5, 9, 20
        Acknowledgment, 17
        Active, 8, 12, 14, 15, 16, 23, 27, 31, 47
        Activity, 5, 8, 11, 13, 14, 17, 26
        Adapter, 1, 6, 24
        Add, 8, 10, 12, 24, 27, 45
        Added, 12, 21, 28, 32, 33, 40, 41, 43, 47, 62
        Adding, 27, 40
        Address, 3, 8, 10, 12, 15, 18, 22, 24, 54, 55, 59
        ADDUser, 8, 12
        ALIAS, 2, 4, 5, 10, 22, 57, 59
        Aliases, 55
        Allocated, 4, 7, 16, 17, 43, 47
        ANALYZER, 47
        ANOD, 37
        Anonymous, 55, 56
        ANSWER, 2, 5, 7, 10, 22, 32, 44, 57
        APpend, 8, 12, 50, 51
        ARchive, 8, 12, 48
        Argument, 12, 16, 18, 20, 21, 22, 25, 29, 32, 33, 40, 54
        Arguments, 55, 56
        ARP, 8, 10, 12, 22, 25, 54, 55
        ARRL, 21, 29, 36, 38, 39, 40, 52, 53
        ASCII, 1, 2, 16, 35, 54
        Autoexec, 45
        AUtokill, 8, 12
        AWLEN, 59

        BACKGROUND, 2, 6, 10, 25, 57
        Backslash, 43
        Backup, 1, 8, 12
        BAckuptim, 8, 12
        BADuser, 8, 12
        Batch, 47
        Baud, 3, 24
        BB, 19
        BBS, 1, 2, 3, 4, 5, 7, 8, 9, 10, 11, 12, 13, 14, 15, 16, 17, 18, 
          19, 20, 21, 22, 23, 24, 26, 27, 28, 29, 30, 31, 33, 35, 36, 37, 
          38, 39, 40, 41, 42, 43, 44, 45, 46, 47, 48, 52, 57, 61, 62
        Bbscall, 45
        BBSLIST, 48, 62
        BD, 58
        BDigi, 8, 13
        Beacon, 6, 8, 9, 13, 19, 21, 45
        Beep, 44, 46
        Bell, 8, 58
        BELLoff, 8, 13
        Bells, 8, 46
        BFRAMES, 2, 6, 57
        BID, 38, 41, 45
        BIDS, 18, 41


                                   64




        BIOS, 22
        Bitrate, 3
        BM, 13
        BMax, 8, 13
        Boot, 1, 8, 13
        Border, 8, 15
        Bottom, 21, 28, 49, 50
        BP, 13
        BPorts, 8, 13
        Bps, 3
        Brackets, 2, 18, 29, 54, 55
        BT, 58
        BText, 8, 13
        Budc, 13
        BUDCall, 12
        BUDCalls, 8, 9, 13, 19, 21
        BUDL, 13
        BUDList, 8, 13
        Buffer, 19, 24, 27, 43, 63
        Buffers, 10, 11, 24, 26, 63
        Bulletins, 31, 41, 42, 45
        BUSY, 13, 14, 37, 38, 44
        Bye, 27

        Call, 1, 2, 4, 5, 7, 8, 10, 13, 14, 15, 19, 20, 22, 23, 28, 29, 31, 
          35, 36, 37, 39, 44, 45, 54, 55, 57, 62
        Callsign, 2, 4, 5, 8, 9, 10, 12, 14, 15, 17, 19, 22, 23, 24, 29, 
          30, 31, 35, 38, 40, 41, 44, 45, 54, 55
        Capture, 14
        Cd, 1, 54, 55, 56
        CGA, 6, 24
        Chan, 10, 14, 27
        CHAnlstat, 14
        CHANNALES, 46
        CHAnstat, 8
        CHART, 1, 55, 60
        CHECK, 2, 5, 8, 14, 17, 31, 39, 41, 61
        CHKMAIL, 1, 47
        CI, 31, 38
        CL, 8, 15
        CLrscrn, 8, 15
        CM, 8
        Cmd, 15, 20, 32, 43, 46, 49, 50, 61
        CMdwindow, 8, 15, 49
        CO, 13
        Color, 1, 2, 6, 7, 8, 10, 15, 25, 61
        Command, 1, 5, 8, 9, 11, 12, 13, 14, 15, 16, 17, 18, 19, 20, 21, 
          22, 23, 24, 25, 26, 27, 28, 29, 30, 31, 32, 33, 35, 37, 39, 40, 
          41, 43, 44, 45, 46, 49, 50, 51, 52, 54, 56, 61, 62, 63
        Commands, 1, 4, 8, 9, 11, 12, 15, 16, 17, 18, 19, 20, 22, 23, 25, 
          26, 27, 28, 29, 31, 33, 39, 43, 45, 49, 50, 51, 54, 55, 56, 62
        Comment, 8, 12, 27, 32
        Comments, 55, 59
        Conference, 27, 28
        Configuration, 2, 28


                                   65




        CONMODE, 59
        Connect, 4, 5, 8, 12, 13, 14, 15, 22, 30, 31, 32, 35, 36, 37, 44, 
          54, 56
        Conversation, 14, 17
        Copy, 1, 8, 13, 15, 44, 47
        CR, 20
        Crash, 44
        Crashes, 47
        Create, 1, 2, 9, 18, 39, 48, 50, 52, 54, 56
        CRetries, 8, 15
        Ctrl, 11, 23, 26
        Currently, 11, 15, 17, 20, 24, 25, 26, 27, 32, 54, 56

        DATABASE, 28, 33, 34
        Databases, 33
        Date, 8, 16, 19, 28, 29, 32, 33
        DBADD, 33
        DEBug, 8, 15
        Default, 1, 9, 10, 13, 14, 15, 16, 17, 18, 19, 20, 21, 24, 33, 47, 
          49, 50, 54, 55, 62, 63
        Defaults, 3, 7, 21
        DEL, 8, 12
        DELE, 55, 56
        DELEfile, 8, 15
        Delete, 8, 12, 15, 18, 29, 47, 48, 49, 50, 51, 52, 55, 56, 61
        DELUser, 8, 15
        DFree, 8, 15
        DIGI, 2, 4, 7, 8, 12, 14, 57
        Digipeat, 4, 22
        Digipeater, 4, 8, 13, 16, 20, 35, 37
        Digipeaters, 8, 9, 12, 14, 19, 28, 29, 35
        DIGipeats, 8, 16
        Diplay, 61
        DIR, 8, 16, 55, 56, 61
        Directory, 1, 8, 9, 10, 12, 13, 15, 16, 18, 21, 23, 24, 28, 32, 33, 
          40, 45, 47, 48, 55, 56, 62
        Disable, 8, 9, 10, 20, 21, 22, 24
        Disables, 10, 21, 25, 43
        Discard, 54
        Disconnect, 5, 8, 14, 16, 17, 27, 46, 54
        Disconnecting, 10, 17, 23
        DISPLAY, 1, 2, 3, 6, 7, 8, 9, 10, 11, 13, 15, 17, 20, 21, 22, 23, 
          24, 25, 26, 27, 29, 30, 32, 33, 41, 61, 63
        Displays, 8, 9, 10, 11, 12, 14, 15, 16, 17, 18, 21, 22, 23, 24, 25, 
          26, 32, 50, 51, 63
        DOcmdfile, 8, 16
        Download, 27, 28, 33, 45
        DPorts, 8, 16, 20, 60
        DTimedate, 8, 16
        DX, 27, 28, 36, 52

        ED, 1, 49
        Edit, 1, 9, 16, 49, 50
        EDITFILE, 1, 16, 50
        Editor, 1, 2, 9, 16, 35, 49, 50, 51, 54


                                   66




        EDITVIEW, 1, 49
        EF, 1, 50, 51, 54
        EFile, 9, 14, 16, 18, 51
        EM, 17
        EMsghdr, 9, 16
        Enable, 6, 9, 10, 13, 21, 22
        Erase, 12, 54
        Error, 1, 15
        Errors, 3, 7, 47
        Esc, 10, 16
        Escape, 16, 49, 50
        EUser, 9, 17
        EUsers, 12
        EXPert, 20, 30, 32
        Expert-Mode, 27

        FBbstimes, 9, 17
        FCall, 9, 17
        Flags, 17
        FO, 17
        FOREGROUND, 2, 6, 10, 25, 57
        Forward, 1, 2, 5, 7, 8, 9, 15, 17, 18, 21, 24, 31, 35, 36, 38, 39, 
          40, 41, 42, 44, 49, 50, 57, 61, 62
        Forwarding, 5, 8, 9, 12, 17, 18, 21, 31, 36, 39, 40, 41, 42, 61
        FRACK, 2, 5, 9, 17, 58, 62
        Free, 8, 9, 10, 15, 17, 21, 24, 62, 63
        FSize, 9, 16, 18
        FTime, 9, 18
        FTImes, 42
        FTP, 18, 54, 55, 56
        FTPgm, 9
        FWD, 9, 21, 24, 39, 40, 51

        Gateway, 4, 8, 16, 58
        Gateways, 9, 19, 28, 29
        Getmsgotd, 9, 18
        GRep, 9, 18, 28
        Guest, 59

        HB, 59
        HC, 1, 18, 52
        HCL, 18, 52
        HClean, 9, 18, 52
        HDrs, 9, 18
        Header, 9, 16, 33, 47, 52
        Headers, 18, 29, 48, 62
        Heard, 4, 9, 19, 21, 27, 28, 29
        HELP, 1, 9, 16, 19, 24, 27, 29, 33, 46, 49, 51, 56
        HF, 20
        HID, 59
        Hierarchical, 21, 39
        HLIMITED, 46
        Host, 58, 59
        Host-id, 18, 54
        HOstname, 9, 18


                                   67




        HOUSECLEANING, 1, 18, 52

        ID, 2, 5, 7, 9, 13, 16, 19, 20, 22, 28, 54, 57
        ID's, 30
        Id-callsign, 23
        Idcall, 41, 42, 45, 52
        IFRAMES, 2, 5, 57
        Ignore, 1, 9, 15, 19, 21
        Ignored, 3, 12, 18, 20, 28, 33, 36, 46, 52
        Initialization, 3, 19
        Installation, 1
        Interface, 1, 3
        Interrupt, 3, 24
        IP, 1, 8, 9, 10, 12, 18, 19, 22, 24, 25, 40, 43, 54, 55, 59
        Ip-address, 12

        JBbs, 9, 19
        JD, 19, 29
        JDigipeat, 19
        JG, 29
        JGateways, 9, 19
        JHeard, 9, 19
        JK, 23, 29
        JKanodes, 9, 19
        JM, 29
        JMsys, 9, 19
        JN, 29
        JNetrom, 9, 19
        JTcp, 9, 19

        K-NODE, 58
        KA, 4, 5, 9, 19, 29, 31, 35, 37, 38, 46
        KANODE, 2, 5, 7, 57
        Kantronics, 5
        KB, 31, 38
        KEybd, 9
        Keyboard, 8, 9, 10, 11, 17, 19, 20, 22, 26, 44, 54
        KF, 29
        Kill, 8, 12, 13, 20, 27, 29
        KIllproc, 9, 20
        KISS, 4, 27, 28, 59
        KM, 29
        KPC-x, 3
        KPorts, 9, 16, 20, 60
        KQ, 38
        KT, 29

        L'string, 30
        LC, 9, 20
        LCount, 9, 20
        LFA, 1, 47, 62
        LIMited, 20, 28, 44, 46, 49, 50
        LINKED, 44
        LL, 13, 29
        LM, 29


                                   68




        LN, 29
        LO, 29
        Local, 8, 11, 13, 23, 24, 26, 54
        Lock, 20
        LOCKkbd, 9, 20
        LOCKUPS, 45
        LOG, 45, 47, 55, 56
        LPT, 3, 22
        LU, 20, 29
        LUsers, 9, 15, 20
        LW, 29
        LY, 29

        Mail, 1, 5, 8, 9, 10, 12, 13, 16, 19, 31, 39, 41, 45, 47, 48, 51, 
          54, 61, 62
        Mailbox, 40
        MAILSIZE, 1, 12, 47
        MAKEP, 58
        MAKEPriva, 9, 20
        Masks, 41
        Max, 13, 38, 43, 46, 51
        Max-BBS-connects, 8
        MAXCHANS, 46
        MAXFRAMES, 2, 5, 9, 20, 58
        Maximum, 5, 9, 10, 12, 20, 22, 46, 47, 49, 50
        MAXRead, 9, 20
        MBL, 32, 41
        MCon, 9, 20, 44
        MDir, 9, 21
        MEM, 43
        Memory, 4, 8, 9, 15, 21, 23, 40, 43
        MERge, 1, 9, 21, 39, 40, 61
        MH, 21
        MHclear, 9, 21
        MKDIR, 55, 56
        MOCOM, 28
        MODE, 1, 4, 16, 27, 28, 30, 43, 46, 49, 50
        Modem, 30
        MONBframe, 9, 21
        MONCC, 21, 43
        MONCF, 21, 43
        MONIFrame, 9, 21
        Monitor, 1, 2, 5, 6, 9, 10, 11, 13, 20, 21, 25, 26, 57, 62
        Monitored, 2, 6, 8, 9, 13, 18, 19, 21, 22, 55, 62
        Monitoring, 8, 9, 10, 13, 18, 21, 22, 24, 43, 62, 63
        Monochrome, 1, 2, 6, 25, 61
        MONOutgoi, 9, 21
        MONPorts, 9, 20, 21, 60
        MONSframe, 10, 21
        MONST, 58
        MONSTats, 10, 21
        MONUframe, 10, 22
        MONxx, 9, 21, 43
        MRESTORE, 1, 47
        Msg, 9, 10, 12, 13, 16, 17, 18, 23, 24, 29, 31, 39, 41, 45, 47, 51


                                   69




        MSGnnn, 47
        MSYSBBSB, 1, 38, 58
        MSYSFWD, 1, 9, 21, 35, 38, 39, 40, 58
        MSYSHOST, 25, 54, 59
        MSYSK, 58
        MSYSPASS, 55, 56, 59
        MSYSTNC, 3, 4, 45, 59
        Multiconnect, 40
        Multiport, 3
        MYAlias, 10, 22
        MYBbs, 10, 22
        MYCall, 10, 22
        MYDIGI, 4, 29
        MYGATE, 4
        MYI, 22, 54, 58
        MYIpaddr, 10, 22, 54
        MYIpaddress, 22, 54
        MYKnode, 10, 22
        Mystery, 29
        MYT, 58
        MYTcpcall, 10
        MYTcpip, 22, 54

        NETROM, 43
        Netroms, 19, 21
        NEWCALL, 39
        NH, 31
        Nicknames, 55
        NM, 58
        Node, 4, 5, 9, 10, 19, 20, 22, 29, 35, 37
        Nodes, 9, 19, 21, 29, 31, 35, 37, 46
        Non-blank, 50, 51
        Non-callsign, 41
        Non-callsigns, 44
        NQ, 30
        NTS, 29, 36, 39
        NUMCHANS, 2, 4, 57
        NZ, 30

        Option, 47, 50
        Optional, 2, 3, 4, 5, 6, 12, 14, 17, 20, 24, 31, 35, 36, 37, 54
        Optionally, 3, 16, 37
        Options, 3, 15
        ORing, 41
        OTD, 18, 58

        Packet, 1, 4, 5, 9, 10, 12, 17, 22, 27, 44, 62
        Packets, 4, 6, 9, 13, 18, 21, 22, 43, 44, 62
        PAClen, 10, 22, 58
        PAGE, 2, 6, 10, 11, 15, 25, 26, 27
        Parameter, 14, 15, 17, 20, 22, 23, 25, 45, 52
        Parameters, 3, 15, 21, 23, 24, 25, 26, 27, 54
        PARITY, 59
        Passall, 59
        Password, 55


                                   70




        Path, 8, 10, 15, 16, 18, 19, 20, 22, 27, 28, 29, 31, 44, 50, 62
        PATTERN, 1, 9, 18, 21, 28, 60
        Pausing, 32
        PB, 19
        PBBS, 5, 19, 58
        PBBS'S, 19
        Performance, 61
        Pf, 21, 22, 31, 39, 53
        PForward, 10, 22
        PIDs, 9, 21
        PORT, 2, 3, 4, 6, 7, 8, 9, 11, 12, 13, 14, 17, 20, 21, 22, 23, 24, 
          25, 26, 28, 29, 31, 35, 37, 54, 57, 58, 60, 61, 63
        PORTS, 2, 4, 6, 8, 9, 10, 13, 19, 20, 21, 22, 24, 28, 46
        Print, 1, 10, 18, 22, 51
        Printed, 18, 46, 50
        Printer, 3, 10, 22
        Printing, 10, 22, 23, 28
        Prints, 10, 22, 47
        PROCESS, 2, 7, 9, 10, 11, 14, 17, 19, 20, 23, 24, 25, 26, 44
        PROcesses, 10, 11, 23, 26
        Processname, 2, 7
        Prompt, 15, 30, 32, 43, 50
        Protocol, 9, 10, 18, 54, 55
        PRTmsgs, 10, 23
        PWD, 55, 56
        PWindow, 10, 23

        QTH, 2, 7, 27, 30, 57
        Queue, 22, 23
        QUIT, 10, 11, 14, 23, 26, 49, 50, 51, 55, 56
        Quote-character, 50

        Radio, 1, 3, 28
        Radios, 19, 20
        RADIOSPEED, 3, 57
        RAWHDLC, 59
        RDir, 10, 23
        Reassign, 19
        Reboot, 45
        Remote, 8, 13, 26, 43
        Remove, 10, 12, 15, 23
        Removes, 8, 10, 15, 17, 23, 56
        REName, 10, 14, 17, 21, 23
        REP, 39, 40, 58
        Replacement, 4, 39, 40
        REPlaces, 10, 21, 23
        RES, 23, 62
        RESponsetime, 23, 62
        RETRIED, 37, 38
        RETRIES, 2, 5, 8, 10, 14, 15, 23, 57
        Retry, 17
        REV, 40
        REVERSE, 40
        RH, 31
        RM, 31


                                   71




        RMDIR, 55, 56
        RMT, 43, 58
        ROM, 9, 19, 29, 31, 35, 37
        Root, 1, 55
        Route, 21, 39
        Routed, 3, 41
        RS, 31

        SB, 31, 44
        Screen, 6, 9, 10, 11, 14, 16, 19, 20, 21, 23, 24, 25, 26, 32, 45, 
          49, 50, 61, 62
        Script, 35, 37
        Scripts, 37
        Scroll, 26
        Scrolling, 32
        SE, 10
        SEnd, 10, 19, 20, 23, 27, 31, 39, 40, 42, 44
        Sendme, 10, 23, 24, 44
        Server, 18, 23, 24, 54
        SETUP, 1, 2, 3
        SFRAMES, 2, 6
        SM, 10, 23, 24
        SMes, 10, 23
        SMTP, 10, 23, 54
        SNow, 10, 24, 33, 34
        SOrt, 10, 24
        SP, 31, 33
        SPEED, 2, 3, 7, 57
        SPmin, 23
        SSID, 2, 4, 5, 8, 12, 13, 14, 17, 22, 35, 54, 55
        ST, 31, 45
        STACK, 2, 7, 23, 44, 57
        Start, 18, 27, 47, 49, 51
        Started, 23, 32, 40
        Starting, 46
        Status, 8, 10, 14, 16, 23, 24, 32, 63
        SU, 24, 63
        Sub-directory, 45
        SUBPORT, 2, 3, 57
        SUspendtrace, 24, 62
        SYSOP, 1, 2, 5, 7, 8, 9, 12, 13, 20, 23, 26, 29, 31, 32, 43, 44, 
          45, 52, 53, 54, 57

        TAbs, 10, 24
        TCP, 1, 8, 9, 10, 18, 19, 22, 25, 40, 43, 54, 55
        TCPIP, 12
        TE, 25, 54
        TELnet, 10, 12, 24, 54, 55
        Time-out, 37
        TImezone, 10, 25, 58
        Title, 13, 30, 31, 33, 36, 41, 52, 53
        TNC, 3, 4, 24, 27, 45, 63
        TNCs, 3, 5, 27, 28
        TNCTYPE, 3, 57
        TOF, 4


                                   72




        Toggles, 10, 25, 32
        TP, 58
        TPorts, 10, 25, 54, 60
        TR, 28
        Trace, 10, 25, 59
        TraceIP, 10, 25
        Traffic, 29, 31, 41
        TRAN, 59
        Txdelay, 62

        UFRAMES, 2, 6, 57
        UI, 9, 21, 22
        Unix, 28, 50
        Unlock, 20
        Uploads, 56
        User, 8, 9, 10, 12, 13, 15, 17, 20, 22, 28, 44, 45, 46, 55, 56
        Username, 55
        USERS, 1, 4, 8, 10, 12, 13, 15, 20, 23, 25, 26, 27, 30, 31, 33, 41, 
          43, 55, 62
        UTC, 58

        VHF, 59
        Via, 3, 4, 8, 14, 22, 31, 35, 37, 38
        Video, 10, 25

        WAtch, 10, 25
        WB, 12, 38, 58
        WBackgrnd, 10, 25
        WC, 15
        WColors, 10, 25
        Weather, 29
        Wforegrnd, 10, 25
        Wildcards, 15, 39
        WINDOW, 1, 2, 6, 7, 8, 10, 14, 15, 23, 25, 26, 49, 57, 61
        Windows, 8, 15, 26
        WN, 28, 32
        WPage, 10, 25
        WS, 11, 26, 57
        WSize, 10, 26


        Yourname, 30
        Yourqth, 30
        Yymmdd, 29

        ZA, 27, 28
        ZB, 27
        ZD, 27
        ZIP, 2, 7, 30, 48, 57
        ZP, 27
        ZR, 27
        ZU, 27





                                   73





























































                                   74